## Slide 1
Improve the physics of the treatment of ET (and hence evaporative demand) in CBRFC operations, and thereby improve water supply forecast skill.
ET = actual evapotranspiration
Cooperate with NWS Western Region Scientific Services Division in provision of scientifically sound, distributed ET-related forecasts to end-users.
CBRFC Evapotranspiration study

## Slide 2
How ET is currently estimated by the NWS River Forecast System
Sacramento-Soil Moisture Accounting (Sac-SMA) model evaporates soil moisture from two depths.
Ep driven by Epan climatology:
  e.g., Jan 1, 1979 = Jan 31, 1979 = Jan 31, 2010
  seasonal data disaggregated to daily,
  missing seasons filled in,
  adjustment factor PEADJ calibrated to water balance.
Wetter years in southern CBRFC region (e.g., San Juan), or when/where Prcp drives Runoff, we under-forecast Runoff, or over-estimate ET.
Option to use time-series in Sac-SMA, down to six-hourly:
  best option is to use observed Ep,
    cannot use Epan at a daily or sub-daily scale,
  best modeling option is a Penman-based estimate,
    heavy on data inputs/parameters.
Ep = evaporative demand
Epan = pan evaporation
Prcp = precipitation

## Slide 3
synthetic measure of evaporative demand to synthesize Epan observations.
mixture of radiation (sunshine and IR) and drying power of the air (humidity and wind).
accounts for instrumentation effects:
  extra sunshine interception by pan walls,
  increased turbulence across water surface.
Physically based models:
PenPan Epan (synthetic pan evaporation)
Epan for April 25, 2010 (mm)
Qn = energy available for ET
U2 = wind speed
esat-ea = vapor pressure deficit (~ humidity)
IR = infra-red, or long-wave radiation

## Slide 4
Preliminary results:
climatology of dynamic daily Epan, Ep, and ETrc – Tenmile Creek, CO
Ep = 0.7 * Epan

## Slide 5
Preliminary results:
dynamic Epan vs. historic simulated streamflow errors

## Slide 6
Preliminary results:
dynamic Epan vs. historic simulated streamflow errors
Concept:
    daily simulated streamflow errors are generated from Sac-SMA/SNOW-17 model in RFC operations, running static Ep (i.e., climatologic monthly),
    errors are compared to dynamic Epan from a 30-year time-series.
Results:
    greatest streamflow errors (+/-) occur with highest Epan at all time-scales to 3-monthly,
    relation is less clear at higher time-scales (monsoon and water supply seasons, annual),
    highest correlation between monthly error and monthly Epan is March/April.
Caveat:
this is one basin:
  Tenmile Creek near Breckenridge, CO
  high-elevation headwater basin,
  snowmelt-dominated.

## Slide 7
adjusts Penman Ep to model seasonality in vapor transfer process through aKP and bKP:
  seasonal functions of day of year,
  calibrated in Kimberly, ID,
  uses regularly forecast meteorological data.
here, ETrc is a specific case of ET calculated for specific biological and physical conditions (a hypothetical reference crop):
well-watered alfalfa/grass of height 0.12 m, rs = 70 sec/m, a = 0.23, rs = 208 sec/m,
uses regularly forecast meteorological data,
international standard (FAO-56).
very commonly used in agricultural community.
Forecasting ETrc across NWS Western Region:
Penman-Monteith ETrc
ETrc forecast for May 3, 2010 (mm)
Kimberly Penman ETrc

## Slide 8
CBRFC & WR-SSD
WFO PRODUCT
ETrc forecast grid
2.5-km resolution
daily/weekly outlook
ETrc point forecast
value-added
statistical context
spatial context
ETrc climatology grids
NLDAS-derived
0.125o resolution
CONUS-wide
daily / weekly
moving window / static weeks
mean
variance
minimum
90% exceedance
median (50%)
10% exceedance
maximum
GFE
script
e.g., http://www.wrh.noaa.gov/sto/et
WFO FORECAST
+ + +
Input forecast grids
NDFD-derived
2.5-km resolution
hourly
Wind
Temperature
Dewpoint
Sky cover
Forecasting ETrc across NWS Western Region:
delivery concept