## Slide 1: SWE & April-July Runoff Volume
Kristen Yeager
Colorado Basin River Forecast Center

## Slide 2: Outline
Motivation
Objective
Results
Conclusions
Future Work

## Slide 3: Motivation & Objective
A CBRFC April 2010 analysis of Lake Powell inflows showed that spring SWE and April-July runoff exhibited a non-linear relationship, prompting questions from stakeholders who expect that “normal” conditions would produce “normal” runoff.
To provide insight on the relationship between spring SWE and April-July runoff volume.

## Slide 4: Colorado—Glen Canyon Dam
0.74738 R2 correlation.
Residual plot shows scatter with no obvious trend—indicative of a linear relationship.

## Slide 5: Colorado—Glen Canyon Dam
Residual plot shows scatter with no obvious trend—indicative of a linear relationship.

## Slide 6: Green—Above Flaming Gorge
0.57421 R2 correlation.
0.65992 R2 correlation without 1983 .

## Slide 7: Yampa—Maybell NR
0.70364 R2 correlation.

## Slide 8: Duchesne—Myton
0.79128 R2 correlation

## Slide 9: Colorado—Lake Granby, Granby NR
0.83629 R2 correlation

## Slide 10: Colorado—Cameo NR
0.70601 R2 correlation.

## Slide 11: Gunnison—Blue Mesa Reservoir
0.76428 R2 correlation.

## Slide 12: San Juan—Bluff NR
0.69158 R2 correlation.

## Slide 13: Weber—Oakley NR
0.75372 R2 correlation.

## Slide 14: Ogden—Pineview Reservoir, Ogden NR
0.8294 R2 correlation.

## Slide 15
In all three scenarios, max-SWE-to-date is the better predictor of April-July runoff.

## Slide 16
The mean date of max SWE is April 8th, approximately three weeks before May 1. Significant melt out has already occurred, thus using the May 1 SWE may underestimate the runoff volume.
PRPC2, SLMC2
BLPU1, HRGU1

## Slide 19: Conclusion and Discussion
Spring SWE and April-July runoff volume display a linear relationship, but not a perfect linear relationship (100% average SWE will not necessarily produce 100% average runoff).
Linearity varies from basin to basin.
Using max-SWE-to-date instead of May 1 SWE does not yield more accurate runoff forecasts for most basins.

## Slide 20: Future Work
What factors may contribute to interannual variability?
Does runoff efficiency (runoff/SWE) vary as a function of spring or winter temperatures?