## Slide 1: National Weather Service River Forecast System (NWSRFS) Interactive Forecast Program (IFP)
CBRFC Open House
August 18, 2010

## Slide 2
Observed Inputs:
Precipitation
Temperature
Freezing Levels
Stage/Flow
Pool Elev/Storage
Forecast Inputs:
Precipitation (5 days)
Temperature (10 days)
Freezing Levels (5 days)
NWSRFS
Operational Forecast System (OFS)
Outputs:
Simulated flow, storage
Short term deterministic forecast flow, storage
Updated model states
Interactive Forecast Program (IFP)
Forecaster:
Quality Control
Analysis
Run-time mods

## Slide 5
Current Time
5/27 18z
Past/observed
Future/forecast
San Juan River at Pagosa Springs
OFS Inputs
Rain/Snow Elevation – determined from freezing levels when available, otherwise calculated from temperatures (more variable)
3 elevation zones
Rain+Melt
Runoff

## Slide 6
Mean Areal Temperature
Mean Areal Precipitation

## Slide 7
Simulated Areal Extent of Snow Cover
Upper zone = 11,000 – 12,700 ft (mean 11,485); 60 mi2
Middle zone = 8,500 – 11,000 ft (mean 9,755) ; 155 mi2
Lower zone = 7,200 – 8,500 ft (mean 7,850) ; 90 mi2
San Juan River at Pagosa Springs
Snow Model States

## Slide 8
Snow Water Equivalent
Areal Extent Snow Cover

## Slide 9
Observed
Simulated
San Juan River at Pagosa Springs
Hydrograph
‘Adjusted’/‘Forecast’ is a single time series broken into observed and future pieces.
  It equals obs when available, otherwise patterned with sim
  Can control how quickly it blends into the actual values of the sim

## Slide 10: Run Time Modifications
Why:
  Input data is not perfect
  Calibration is not perfect
  Models are not perfect
Most commonly used at CBRFC:
  Time series
    Set data to missing
    Change values - TSCHNG
      Precipitation
      Temperature
      Diversions
    Change the blend period
    Set reservoir releases - SETQMEAN
  Snow model
    Change the amount of snow water equivalent
    Change the areal extent of snow cover
    Increase or decrease melt with a ‘melt factor correction’ - MFC
    Force precipitation type to rain or snow
  Soil moisture model
    Change the contents of tanks

## Slide 12
Simulated flow now tracking observed flow better after MFC mod
Forecast flow higher than before
San Juan River at Pagosa Springs
Hydrograph after mod

## Slide 13
IFP COMPANION

## Slide 14
Rio Blanco River near Pagosa Springs
Hydrograph with diversion
Observed
Simulated flow after diversion subtracted
Observed diversion
Future diversion – holds last observed value constant
Unregulated – sim flow before diversion subtracted

## Slide 15
Future diversion – hand-drawn by forecaster to estimate how it will likely behave
(TSCHNG mod)
Simulated flow after diversion subtracted –
now more consistent with past flow
Rio Blanco River near Pagosa Springs
Hydrograph with TSCHNG mod
for future diversion

## Slide 16
Flow routed from upstream
segment
Model calculated consumptive use
Observed
Local simulated = addition to flow below upstream segment(s)
Final simulated =
Routed + Local – Cons use
Los Pinos River at La Boca
Hydrograph with Routed flow, Local sim, and Cons use

## Slide 17
Navajo Reservoir Inflow
Hydrograph with routed flow
Los Pinos – La Boca
Piedra – Arboles
San Juan –
Carracas
Observed inflow
Local sim
Total routed
Final simulated =
Total routed + Local

## Slide 18
Navajo Reservoir
Pool Elevation
Observed pool elev
Adjusted pool elev – equals obs when available, otherwise patterned with sim
Simulated
pool elev

## Slide 19
Navajo Reservoir
Outflow – standard
SETQMEAN mod
Diversion taken straight out of reservoir – does not affect release values, but needed to simulate pool elevation correctly.
Observed release from dcp (primary)
Obs release from Reclamation
Simulated release explicitly set to the observed values in the past and the last obs value for the future (SETQMEAN mod)
Adjusted – equals obs when available, otherwise patterned with sim

## Slide 20
Navajo Reservoir
Outflow – release schedule in SETQMEAN mod
Simulated release explicitly set to the observed values in the past and an agency defined release schedule for the future (SETQMEAN mod)

## Slide 21
Navajo Reservoir
Outflow – reservoir rules
(no SETQMEAN mod)
Simulated release not set in the past or the future – model simulation is based on reservoir rules
Adjusted – the blend period to the simulation has been set very short