## Slide 1
Temperature and Precipitation Data
CBRFC Stakeholder Forum
July 31, 2012

## Slide 2
PRECIPITATION DATA– WHY IS THIS IMPORTANT ?
Primary Impacts:
Immediate runoff from rainfall events
Affects soil moisture conditions and seasonal volume forecasts
Combined with temperature to build snowpack in the model
A direct input into the operational soil moisture & snow model
TEMPERATURE DATA– WHY IS THIS IMPORTANT ?
A direct input into the snow-17 operational model
Primary Impacts:
Determine precipitation type -> builds the snowpack
Energy and heat transfer properties:
Extent of snow cover
When the snowpack ripens in the spring
Process of melting the snowpack

## Slide 3
Selection of Temperature & Precipitation Stations Starts with Calibration of the Model
Data Site Requirements:
Relevant location to the river basin and sufficient historical period of record.
Must be stable through time (spent weeks verifying this through double mass analysis)
Maintain consistency between calibration and daily operations (use same data sites)
These requirements above tend to eliminate many candidates
Simulated
(yellow)
Observed
(blue)
Simulated
(yellow)
Observed
(blue)

## Slide 4
DATA NETWORKS
SOURCES (Precipitation)
ALERT Networks (Automated Local Evaluation in Real Time-Radio)
GOES Data Collection Platforms (DCP) – includes Upper Colorado Network/RAWS/etc.
SNOTEL *
Cooperators *
CoCoRaHS (Community Collaborative Rain, Hail & Snow Network)
NEXRAD (Radar Products)
Satellite Derived
GOES Data Collection Platforms (DCP) – includes Upper Colorado Network/RAWS/etc. *
SNOTEL *
Cooperators *
SOURCES (Temperature)
* Data sources for model calibration

## Slide 5
ALERT & CoCoRaHS
Precipitation Data
GOES DCP Precipitation Data

## Slide 6
SNOTEL Precipitation Data
Cooperator Network

## Slide 7
All Precipitation Sites

## Slide 8
GOES DCP Temperature Data

## Slide 9
Cooperator Network Temperature Data

## Slide 10
SNOTEL Network Temperature Data

## Slide 11
All Temperature Data Networks

## Slide 12
Precipitation gauge sites used in our model for the San Juan Basin (subset of all available)
calibrate and run operationally with the same data (260 sites for CBRFC)

## Slide 13
Temperature sites in the model for the San Juan Basin
Calibrate and run operationally with the same data (330 sites for CBRFC)

## Slide 14
Additional Precipitation Source – NEXRAD Radar Derived Precipitation
No radar coverage Much less in winter

## Slide 15
Hourly radar precipitation data is used in southern Utah, Arizona, and New Mexico (1-hour segments)
The option exists to use radar precipitation data in northern Utah and Colorado during summer months
(6-hour segments)
Areas where radar precipitation data may be used (rainfall-runoff hydrology dominates) as input to the hydrologic model.

## Slide 16
Radar derived precipitation and gage precipitation are combined to generate an hourly gridded product ingested by our hydrologic model
Precipitation Source – Hourly Multi-Precipitation Editor (MPE generated Precipitation)
Satellite derived precipitation is available

## Slide 17
Goal: Combine all precipitation sources into to a coherent precipitation product

## Slide 18
… same goal with temperature

## Slide 19
Quality Check All Data
- Use all sites all sources
- Meteorological situation
- Affects gauge performance
- Expected precipitation patterns
False
Goal: Combine all precip & temperature data sources into a coherent product

## Slide 20
Quality Check All Data
- Use all sites all sources
- Meteorological situation
- Affects gauge performance
Convert point 24/6 hour gauge data, to a Mean Areal Precipitation value (MAP). Uses only a subset of all sites available. Time step = 6 hours.
So what gets in the Model (and Forecast) ?
Observed data (and Forecast precipitation & temperature ) are re-evaluated by forecaster interacting with the model during the daily operational run.
Incorporates radar data (MPE) to create a Mean Areal Precipitation (MAP) value. Time step = 1 hour.
Convert point data to Mean Areal Temperature (MAT). Time step = 6 hours.

## Slide 21
Upper (11000-12644)
Middle (8500-11500)
Lower (7067-8500)
El Diente Peak (EDSC2) SNOTEL (.34)
Lone Cone (LNCC2) SNOTEL (.17)
Scotch Creek (SHSC2) SNOTEL (.34)
Cortez (CTZC2) Precipitation (1.2)
Lizard Head (LIZC2) SNOTEL (.55)
El Diente Peak (EDSC2) SNOTEL (.55)
EDSC2
(10,200 ft)
LNCC2
(9600 ft)
SHSC2
(9100 ft)
LIZC2
(10,200 ft)
CTZC2
(6153 ft)
Dolores – Dolores (DOLC2) Segment (below Rico)
SAC-SMA Model Sub-Areas
Stations used to compute precipitation & their weighting
(locations approximate)
Dolores- Rico Segment (DRRC2)
What is a MAP? Example of Stations used to generate Mean Areal Precipitation

## Slide 22
Operational Model Run 07/25 Noon-6 pm Precipitation for Dolores @ Dolores

## Slide 23
Operational Model Run 07/25 6pm-Midnight Precipitation for Dolores @ Dolores

## Slide 24
Operational Model Run for Dolores @ Dolores / Precipitation 07/25 Noon-Midnight
Model simulated
Observed

## Slide 25
6/24 hour gauge data is used to create MAP’s in the Great Basin and Upper Colorado Basin

## Slide 26
Temperature and Precipitation observing networks are critical as they provide direct inputs into our hydrologic models and drive the streamflow forecasts.
  Immediate direct runoff (rainfall-runoff situation)
  Soil moisture states (long term volumes & peaks)
  Snowpack
Maintaining existing networks is critical to our forecast abilities
  Great deal of effort verifying gauge is stable through time.
  Priority given to those sites utilized in calibration / long period of records
    SNOTEL Network our most critical network
  The loss of any site risks degradation of overall data quality & resulting forecasts
  Surface network especially critical in West due to radar limitations
Consequences of bad (or limited data) are somewhat obvious
  Negatively impact ability to quality control observed data
  Misrepresentation of snowpack (seasonal & peak flow implications)
  Incorrect classification of precipitation types (further impact model states)
  Results: Poor model simulations, missed flood events, poor seasonal forecasts.
SUMMARY