## Slide 1
What Affects Forecast Quality
Uncertainty in weather forecasts
Data
Network density
Quality of measurements
Missing measurements
Loss of data sites used in calibration
Diversions & consumptive use
Model calibration errors (usually tied to historical data)

## Slide 2: Precipitation Network (~3000 stations)
NRCS (SNOTEL and SCAN)
COOP
RAWS
ALERT (several counties in AZ, NM and NV)
USRCRN
USCRN
ASOS
AWOS
UCN
COCORAHS

## Slide 3: Precipitation Network
Periodically update the metadata
  Mainly latitude, longitude and elevation
  Additional check using 30 meter DEM data
  Goal is to remove obvious errors
  Done about once each year
  Important for precipitation analysis
  Important for radar bias calculation

## Slide 5
Radar coverage depends on Freezing Level
Adjusting for bias depends on gage network density

## Slide 6: Precipitation Network
Upper Colorado
  Winter: use predetermined station weights
  summer : use all stations including radar, but limit the radar where the mid beam is < 8000 AGL
Lower Colorado
  winter : Use all stations including radar but only use radar in areas where it is raining. This results in only using gauges in most areas
  summer : use all stations including radar, but limit the radar where the mid beam is < 8000 AGL

## Slide 7
January 2010 Heavy Rain Event
Oak Creek

## Slide 8
January 21-22 2010 Observed Precipitation

## Slide 10
SNOTEL Site: Mormon Mountain
Precip Type – Remained as snow

## Slide 11
SNOTEL Site: Mormon Mountain

## Slide 12
Large runoff forecast indicated but response was minimal
Never had a good handle on the freezing level, rain/snow line (critical in AZ)
Good data network exists but lower elevation SNOTEL might have helped
Data network limits & uncertainty in future weather (misplaced QPF & challenging Freezing Level) resulted in missed forecast
January 2010 Heavy Rain Even - Oak Creek