## Slide 1
Modeling Updates
CRFS—Technical Meeting
November 14, 2012

## Slide 2: Forecasting and Modeling Updates
24-Month Study
  Recent Enhancements (implemented May 2012)
  Potential Enhancements
Mid-Term (Probabilistic) Operations Model (MTOM)

## Slide 3: Recent Enhancements (implemented May 2012)

## Slide 4: 24-Month Study Recent Enhancements
No changes to methods or modeling assumptions
No changes to model results
Purpose of enhancements
  “Clean Up” Model Workspace
  Improve Transparency, Consistency, Efficiency

## Slide 5: 24-Month Study Recent Enhancements
“Clean Up” Model Workspace
  Remove unused data objects
  Remove “unused” and misleadingly named reach object
Improve transparency of model
  Rename objects to more intuitive and descriptive names
Make 24-Month Study and MTOM more consistent
  Yearly data slots vs repetitive monthly data slots
Added efficiencies to process
  Ruleset in “reverse” priority order
  Added Lower Basin Surplus rules
Notes: Surplus rules: now we don’t have to manually enter the schedules into the model and sets the surplus operation.

## Slide 6: Potential Enhancements

## Slide 7: 24-Month Study Potential Enhancements
Lees Ferry Intervening flows
  Changes to reporting
  Changes to model configuration to support reporting
No changes to methods or modeling assumptions
No changes to model results
Purpose of enhancements
  More accurately project future flow at Lees Ferry streamgage
  Fix “double reporting” of historic flows between Glen Canyon Dam and Lees Ferry streamgage
  Improve transparency and consistency

## Slide 8: 24-Month Study Report Lake Powell Page
Lees Ferry Column
  Current:
  Future Flow = GCD release
Potential Change:
Future flow = GCD release + 5-yr avg of intervening flow

## Slide 9
Side Inflow Column
  Current:
  Side Inflow = 5-yr avg of (side inflows above Lees Ferry + side inflows below Lees Ferry)
Potential Change:
Side Inflow = 5-yr avg of side inflows below Lees Ferry
24-Month Study Report Lake Mead Page

## Slide 10
Add additional Reach to PowellToMead Aggregate Reach
  Separates out flows
  Sum of reaches remains the same
Modify Data Management Interfaces (DMIs)
  move data from model to report
24-Month Study Model Configuration
“Mock up” of potential change to model

## Slide 11: 24-Month Study Potential Enhancements
Lees Ferry Intervening flows
  Changes to reporting
  Changes to model configuration to support reporting
No changes to methods or modeling assumptions
No changes to model results
Potential Implementation: Jan/Feb 2013

## Slide 12: Questions?