## Slide 1: Water Year 2015 Review
CRFS
December 8, 2015

## Slide 2
Soil Moisture – Entering The 2014/2015 Winter

## Slide 3
Fall Weather: Mostly warm and dry

## Slide 4
Winter/Early Spring:
Dominated by dry/warm pattern

## Slide 5
Winter Temperatures: Record heat
Impacts:
Highly variable snowpack - (Rain falling during typical snow periods)
Winter snow melt – especially lower / middle elevations
Early depletion of the snowpack – lead to record low SWE in early April / May

## Slide 6
July:
Above average precipitation widespread
May:
Widespread heavy rain with some areas receiving 200 to more than 400 percent of average.
San Juan 6-11 inches of precipitation
June:
Significant precipitation continues for Gunnison basin and south
A big change in the weather:
Frequent moist storm systems (tropical moisture source)
Much below average temperatures May into early June

## Slide 7
Colorado River above Lake Powell: SNOTEL Precipitation Rankings
January through April 2015
May through July 2015
Many sites driest 1-2 on record
Many sites wettest 1-3 on record

## Slide 8
Green River Basin
April-July 2015
Observed Volume
% of 1981-2010 avg
Upper Green
- Below average snow
- Early melt in March/April due to warm temperatures
- Wet May, snow accumulation/retention at high elevation
Yampa
- Near record low snow conditions
- Extremely wet May
- Rain was a larger contribution to seasonal volumes than snow at some points
Duchesne
- Record low snow conditions
- Wet May (rain at low elevations, snow at high elevations)
- April-July observed were double May 1st forecasts at some points

## Slide 9
Upper Green: Basin Conditions
% of 1981-2010 avg

## Slide 10
767 KAF
106% avg

## Slide 11
1035 KAF
106% avg

## Slide 12
Local = Flaming Gorge Inflow - Fontenelle Inflow
Regulated Flow from Viva Naughton, Meeks Cabin, Stateline, and Big Sandy Reservoirs
Model guidance was not great
Always a source of uncertainty
Upper Green: Flaming Gorge Local

## Slide 13
April
May
June
July
Above average precip for four months
Reservoirs spilled due to high/under predicted inflows
Reduced demand/use
Late snow accumulation and retention
 | Blacks Fork-Little America |  | Henry's Fork | 
 | ESP | OBS | ESP | OBS
Jan | 125 | 124 | 26 | 67
Feb | 81 | 124 | 24 | 67
Mar | 83 | 124 | 21.5 | 67
Apr | 38 | 124 | 13.1 | 67
May | 35 | 124 | 20 | 67
Upper Green: Flaming Gorge Local

## Slide 14
Yampa: Basin Conditions
% of 1981-2010 avg

## Slide 15
2015
Snow= 65% of Seasonal Precipitation
Normal
Snow= 95 % of Seasonal Precipitation
1042 KAF
84% avg

## Slide 16
Duchesne: Basin Conditions
% of 1981-2010 avg

## Slide 17
71 KAF
66% avg

## Slide 18
Upper Colorado Basin
April-July 2015
Observed Volume
% of 1981-2010 avg
Mainstem
- Coming off a very good 2014 runoff season
- Above to much above average winter base flows
- Headwaters fared better precip-wise during the winter than much of the Upper Basin
- Total transmountain diversions were ~50% of average during WY2015
Gunnison/Dolores
- Large forecast errors, but model performed as expected

## Slide 19
Upper Colorado Mainstem: Basin Conditions
% of 1981-2010 avg

## Slide 20
2348 KAF
99% avg
198 KAF
121% avg

## Slide 21
Gunnison: Basin Conditions
% of 1981-2010 avg

## Slide 22
708 KAF
105% avg

## Slide 23
Jan: 690 KAF (102%)
Feb: 620 KAF (92%)
Mar: 600 KAF (89%)
Apr: 480 KAF (71%)
May: 440 KAF (65%)
June: 570 KAF (84%)
July: 700 KAF (104%)
1st of month Forecasts
April-July Observed
708 KAF (105%)
Blue Mesa Reservoir Inflow Forecast Progression 2015
50% Chance of Exceeding: 440 KAF
10 % Chance of Exceeding : 540 KAF
90 % Chance of Exceeding: 370 KAF
May-July precipitation at SNOTEL sites was in the top 3-6% of the historical record.
Model / Forecast Performance & Uncertainty
Highest Forecast Trace on May 1 was 741 KAF: (3% exceedance probability)
Second Highest Forecast Trace on May 1 was 604 KAF: (7% exceedance probability)

## Slide 24
111 KAF
112% avg
94 KAF
93% avg

## Slide 25
Dolores: Basin Conditions
% of 1981-2010 avg

## Slide 26
226 KAF
77% avg

## Slide 27
San Juan Basin
April-July 2015
Observed Volume
% of 1981-2010 avg
San Juan
- Record (300% to more than 400% average) precipitation across the basin during May
- Much above average precipitation (200%-300%) continued into June

## Slide 28
San Juan: Basin Conditions
% of 1981-2010 avg

## Slide 29
619 KAF
84% avg

## Slide 30
205 KAF
106% avg
54 KAF
97% avg

## Slide 31
439 KAF
106% avg

## Slide 32
Lake Powell
April-July 2015
Observed Volume
% of 1981-2010 avg
Lake Powell
- Largest May-June forecast change:
 +2000 kaf (67% volume change)
- Largest May forecast vs. observed difference:
 3700 kaf (124% volume difference)

## Slide 33
Chart: 
| Monthly Precipitation | Water Year Precipitation | Snow Water Equivalent | Monthly Inflow | Forecast
As of Jan 1, 2015 | 118 | 84 | 103 | 113 | 91
As of Feb 1, 2015 | 61 | 79 | 85 | 96 | 73
As of Mar 1, 2015 | 74 | 79 | 82 | 108 | 71
As of Apr 1, 2015 | 61 | 76 | 61 | 83.0349 | 52.3743
As of May 1, 2015 | 83 | 77 | 47 | 60.4947 | 41.8994
As of Jun 1, 2015 | 244 | 98 | 68.8225 | 69.8324
Lake Powell: Basin Conditions
% of 1981-2010 avg

## Slide 34
Green – Green River, UT
Colorado – Cisco, nr
San Juan – Bluff, nr
2520 KAF
85% avg
4113 KAF
93% avg
1049 KAF
95% avg

## Slide 35
6712 KAF
94% avg
3000 KAF
42% avg

## Slide 36
Chart: 
| Green | Other | San Juan | Headwaters
2015 Observed Inflow | 0.31488 | 0.039985 | 0.1312 | 0.51393
January %Avg Forecasts
Green – 95%
Colorado – 98%
San Juan – 65%
Powell – 91%
April %Avg Forecasts
Green – 54%
Colorado– 68%
San Juan – 40%
Powell – 52%
May %Avg Forecasts
Green – 48%
Colorado– 58%
San Juan – 27%
Powell – 42%
2015 %Avg Observed
Green – 85%
Colorado– 93%
San Juan – 95%
Powell – 94%
Lake Powell: Contributing Flows
April – July Unregulated Inflow

## Slide 37: Lower Colorado Basin
Virgin
Lower Basin
- Neutral ENSO conditions
- The wet spring did not improve conditions in Arizona; only slight improvement in Virgin Basin
- Virgin River at Virgin 3rd driest on record this year (after 2nd driest last year)

## Slide 38
21 KAF
36% avg

## Slide 39
137 KAF
100% med
159 KAF
102% med
Salt – Roosevelt, nr
146 KAF
47% med
Gila – Solomon, nr, Head of Safford Vly
Verde – Tangle Ck, blo, Horseshoe Dam, abv

## Slide 40
What can we take-away from 2015?
Forecast/Model errors exist - Calibration Data, Observed Data, Future Weather
Model in general performed as expected in many areas with large April and May
forecast errors. The extreme conditions were caught within the full forecast
distribution even though we weren’t focusing on that type of scenario developing.
The ability to catch such future weather extremes in water supply forecasts is very
limited. It depends upon if these events exist in the calibration period used. Also
requires improved and quantifiable longer-term seasonal climate forecasts.
The spring rain coming when it did, following lower elevation melt that increased
soil moisture conditions, resulted in more efficient runoff.
Late season high elevation snow carries a lot of uncertainty. There is limited to no
ground truth and the use satellite data this past spring was limited due to extended
and extensive cloud cover.
Unmeasured depletions from the river systems were lower than typical due to
reduced demands. This extra water showed up in the final observed volumes at
many sites.