## Slide 1: CBRFC Postmortem Analysis on June 2010 flooding in UT and CO

## Slide 2: Post-Mortem for June 6-10 flooding
Forecasts generally poor and under simulated for peak flows that occurred June 6-10, 2010 in northern Utah and western Colorado
General conditions leading into event:
  Near normal/below normal snowpack and precipitation on June 1
  Very cool May
  Warm (but not record), moist air mass beginning June 5
  Temperature forecasts generally good
  SNOTEL sites in flooding catchments near average for this time of year
  Streamflow forecasts were almost uniformly too low
What happened in the real world?
What happened in the model world?

## Slide 3: Temperature

## Slide 4: Recent local Temperatures
May was generally cool, delayed melt
First week in June was warm
From
NOAA CPC
A cool May
A warm week

## Slide 6: Snow

## Slide 7
Snow:
May 6 (above)
June 4 (right)

## Slide 10: Streamflow Forecasts

## Slide 11: Observations
Assumption that Peaks=f(snow volume)
Season volumes affected somewhat
Seen on:
  Roaring Fork
  Eagle
  Uncompahgre (a little)
  Granby (a little)
  Yampa
  Big/Little Cottonwood
  Headwaters of Provo/Weber/Bear/Uinta streams
Did not affect
  Gunnison/San Juan Rivers
  Blue
  Upper Green

## Slide 17: Streamflow Year Comparisons
Both 2005 and 2006 had bigger snowpacks
Flow peaks in prior years occurred after lower snow was gone
In 2005 and 2006, imagine combining the two melt pulses into one – you’d get a flood!
2010
2005
2006
Rainfall

## Slide 18: Little Cottonwood at Crestwood Park flow forecasts under-simulated
forecasts
observed
simulated
bankfull
flood
weekend

## Slide 19: WFO Watches and warnings for Little Cottonwood (Cottonwood, Crestwood Park hydrograph shown)
Flood Warning
543 PM MDT SUN JUN 6
Hydrologic Outlook (ESF)
330 PM MST SAT JUN 5
“FLOODING IS NOT ANTICIPATED”
Flood Watch
1132 AM MDT SUN JUN 6
weekend

## Slide 20: Snotels in Cottonwoods
Mill-D North (8960’, southwest face)
  “middle”
Brighton (8750’, southeast face)
  “middle”
Snowbird (9640’, northeast face)
  “high”
Snowbird
Mill-D North
Brighton

## Slide 21: SWE in Cottonwoods
Nearly identical melt!
2006
2010
Snowmelt rate extraordinarily large? (no)
Snowmelt extraordinarily late? (no)

## Slide 22: Snow Distribution – corroborates presence of lower elevation snow in 2010 at start of event
2006 Snowbird SNOTEL trace almost identical to 2010 trace from June 1-10
However, NOHRSC indicates south facing slopes had already melted out in 2006
2010 June 1
2006 June 1, for comparison

## Slide 23: SWE melt comparison
Compared to 2005 and 2006: 2010 had less SWE, but melt was more synchronized
2010
2005
2006
Lower vs upper meltout
20 days
30 days
5 days

## Slide 24: Little Cottonwood at Crestwood Park: Temp. forecasts
forecasts
observed
Averaged over all elevation zones: not bad!
weekend

## Slide 25: SWE/Snotel Comparison
June Snowmelt at Snowbird in 2006 & 2010 were similar, but in 2006, snow at lower elevations was gone – in 2010 there was synchronized, rapid melt at both elevations.
What about May 2006, when both zones were also melting? Melt rates were lower, particularly in upper zone (and flow response was smaller).
2010
~1.8 in/day
~2 in/day
~1.5 in/day
2.5 to 3 in/day
2006

## Slide 26: What did the model think?
Model SWE at time of runoff was sufficient, and melt rates were close to observed rates
Overall shape of seasonal snowpack was good (compare to ~38’ peak at Snowbird)
2.8 in/day
2.6 in/day
Jun 3-8

## Slide 27: What did the model think?
Model soil was on pretty dry in upper and middle levels entering event, and stored water
Deficits in model soil filling
Jun 3-8
3-4 days melt
soaked up
upper
lower
middle

## Slide 28
Was the model right about soil moisture?
Partly right – 2010 was relatively dry
Partly wrong – throughout winter, SM steadily moved upward toward normal levels
  In model, this recovery started late and didn’t get as far
  3-4 days of melt went by before model really started generating runoff

## Slide 29: SWE related mods? LCTU1 (Cottonwood @ SLC) only melt factor was used
MFC 0.69
CFS
MFC 1.70
MFC 1.80 – deleted 6/7
MFC 2.35 – deleted 6/8, 6/10
MFC 1.47 – deleted 6/9
Note, appears we did only one soil water mod during May-June

## Slide 30: Preliminary Thoughts (circa June 2010)
The snowmelt that drove the flooding was …
  More rapid than normal
  From more area than normal (both middle and high elevations; also south facing and north facing at the same time)
The cool May 2010 …
  Delayed the melt of snow into June, holding lower elevation snow
  Atmospheric moisture effects contributed little during the event, but prior month of cool, relatively moist conditions may have helped it ripen
CBRFC models under-simulated the streamflow response

## Slide 31: Questions
Hypothesis #1: Existing model infrastructure not sufficient to capture this event.
  H1A: Mismatch between real time and calibration precipitation and temperature input?
  H1B: Insufficient model spatial distribution? E.g. Model differentiates elevation but not aspect.
  H1C: Insufficient physics in (temperature index) snow model?
Hypothesis #2: Existing observational infrastructure not sufficiently distributed in space to capture this event.
Tested by extending calibration dataset for Weber Basin through 2010 (Craig)
Result: did not significantly alter streamflow simuation
Tested by expanding number of “zones” in Weber Basin model to reflect aspect (Craig)
Result: Improved simulation somewhat but not dramatically

## Slide 32
Possible Reasons
Possible Input errors
  Precipitation
  Temperature
    Fixes for the future
  However, running model in calibration mode showed similar errors
    Show results
Known Snow-17 errors in anomalous situations
  Temperature index model
Melt of snow probably was atypical
  Diurnal amplitude/SCE tells us something
  Model is split by elevation zones not aspect
    Significant melt in May in exposed areas
    Delay of melt in colder, less exposed areas
      North facing lower level melted at same time as south facing high level?
      Preliminary re-calibration results not much help
        Added more zones
        Made sac-sma more responsive
Similar errors in other years

## Slide 33
Areas of Study
Areal Extent updates
  Incorporate Snow Cover Extent into model
Improvements to the Snow model
  Pursue alternatives to SNOW-17
Distributed models
  Finer scale modeling may be the only answer
Late melt = flooding potential