## Slide 1: Overview of CBRFC Flood Operations Arizona WFOs – May 19, 2011
Kevin Werner, SCH

## Slide 2: Outline
Basics of RFC hydrologic model
Model inputs
Challenges during events
  Examples during the December 2010 event
Dam Failures
How RFC and WFO work together
In the Future

## Slide 3: Forecast Process
Forecast
precip / temp
Weather and Climate Forecasts
River
Forecast
System
parameters
Observed
Data
Analysis &
Quality Control
Calibration
model
guidance
Hydrologic Model Analysis
hydrologic
expertise &
judgment
Outputs
Graphics
River Forecasts
Decisions
Rules, values, other factors, politics

## Slide 4: RFC Forecast System
Snow Model: SNOW-17 Temperature Index Snow model
RFC forecast uses a snow model and a rainfall-runoff model:
  SNOW-17: Temperature index model for simulating snowpack accumulation and melt
  Sacramento Soil Moisture Accounting Model: Conceptual hydrologic model used to generate runoff

## Slide 5: RFC Model Inputs
Observed
    Precipitation (radar and gages)
    Streamflow
    Temperatures
    Freezing levels
Forecast
    Precipitation (5 days, from HPC or WFOs)
    Temperatures (10 days – MOS)
    Freezing levels (RUC)

## Slide 6: QC Observed Precip/Temp
Mountain Mapper (MM) for 24 hour and 6 hourly amounts (point data), and min/max temp
Multi-sensor Precipitation Estimator (MPE) for hourly (incorporates gage data from MM and radar)
 feeds hydrologic model

## Slide 7: QPF
Point Values
(HPC)
Grid Values
(Prism
Scaling)
Basin Values
Use GFE to view WFO QPF
 Will very soon feed hydro model
CBRFC relies on WFO
QPF expertise during
Hydrologic events

## Slide 8: Influence of Inputs on River Forecast
QPF!!
    Amount, timing, distribution and location all affect the streamflow forecast GREATLY
Freezing levels for some storms
    Dictates snow or rain
Data availability during an event
Forecast temperature for snow melt

## Slide 9: Challenges during events
DATA!!
  Streamgages malfunction or get washed away during high water events
  Precip data not always representative
    ALERT data was an issue in December

## Slide 10: Challenges during events - cont
Rating tables shift
  Scouring
  Debris
Updated daily
Updated during events

## Slide 11: Issues during events – cont
Rating tables shift, especially during events
  Model uses flow derived from stage, and then converts back to stage for the forecast

## Slide 12: Contingency Runs
Phone call to discuss potential QPF or freezing level scenarios
RFC provide contingency runs, accessible though hydrograph on web site

## Slide 13: Working together
RFC  WFO
Bad streamflow data
  Currently weekly notification
  Program to alert during event
Rating table changes
  Daily program
  Need to figure out what to do during events
Quality of simulation
WFO  RFC
Reports on the ground impacts
Significant changes to QPF
Confidence in QPF/forecast freezing levels/temps
  Contingency runs
Extended staffing – CBRFC will extend hours for events as needed and upon request from WFO management
Call us if you have questions

## Slide 14: In the future…
CHPS – Community Hydrologic Prediction System: Parallel Operations now; Operational by Oct 1, 2011
Distributed modeling – better representation of areal distribution of precipitation
Ensemble forecasts – HEFS being run experimentally now

## Slide 15
CHPS
CHPS – Community Hydrologic Prediction System
  The whole system, ie data collection, quality control, future forcing creation
  Includes FEWS
FEWS – Flood Early Warning System
  The hydrologic modelling software
  Within CHPS
  Replaces NWSRFS

## Slide 16
Current IFP interface with NWSRFS

## Slide 17
New IFD interface for FEWS
Highlights of new features
More logging of system
Easier navigation of model plots
Better integration of segment information
Ability to view all data in system

## Slide 18
Gridded data into FEWS QPF example

## Slide 19
Gridded Temperatures and Freezing Levels will be imported too

## Slide 20: Example Short Range Ensemble Products
7 of 13 RFCs are now producing an operational short range ensemble forecast product
Example -- Russian River – Guerneville, CA (GUEC1), December 24-29, 2010
  2 upstream reservoirs,
  5 locals
  5 routing reaches
  Following slides from Rob Hartman, Hydrologist in Charge
  California-Nevada River Forecast Center (CNRFC)

## Slide 21: GUEC1 – 12/24/2010
X
X

## Slide 22
GUEC1 – 12/25/2010
X
X

## Slide 23
GUEC1 – 12/26/2010
X
X

## Slide 24
GUEC1 – 12/27/2010
X
X

## Slide 25
GUEC1 – 12/28/2010
X
X

## Slide 26
Beta CBRFC Website
Main page -> beta map
Seeking input

## Slide 27: Discussion
Current and future RFC modeling and forecasting capabilities – Are you using these effectively?
CBRFC website retooling – Any input?
How can new services / tools be applied in the WFO and to stakeholders?

## Slide 28
Kevin Werner
CBRFC Service Coordination Hydrologist
Phone: 801.524.5130
Email: michelle.schmidt@noaa.gov
Feedback, Questions, Concerns always welcome….
www.cbrfc.noaa.gov