## Slide 1
Kevin Werner
NWS Colorado Basin River Forecast Center
CBRFC Forecasts and Updates

## Slide 2: Outline
Current Forecast / Conditions
Ensemble Streamflow Prediction (ESP) Primer
30 year average period update

## Slide 3
Web Reference: http://www.cbrfc.noaa.gov/gmap/gmapm.php?scon=checked
Snow
April 7 as a percent of average (above)
April 7 as a percentile (right)

## Slide 4
~25 sites showing highest value ever for today!!

## Slide 5
Web Reference: www.cbrfc.noaa.gov/gmap/gmapm.php?wcon=checked
April 1, 2011
Water Supply Forecasts
Highlights:
Wet winter continues for much of the basin with many forecasts higher than any year since 1997
Some northern basins predicting flows near the top 10%
Forecasts slightly higher across northern basins since Feb 1 and Mar 1
San Juan and lower basin somewhat lower since Feb 1 and Mar 1

## Slide 6
Web Reference: www.cbrfc.noaa.gov/gmap/gmapm.php?wcon=checked

## Slide 7
YEAR | OBS VOL (KAF) / %AVG | RANK (101 YRS)
2005 | 8844 / 112% | 39
2008 | 8909 / 112% | 38
1993 | 9984 / 126% | 29
Lake Powell historical inflows

## Slide 8: Water Supply Forecast Methods
Statistical Forecasting
  Statistical Regression Equations
  Primary NOAA/RFC forecast method from 1940’s to mid 1990’s.
  Primary NRCS/NWCC forecast method
  Historical Relationships between flow, snow, & precipitation (1971-2000)
  Tied to a fixed runoff period (inflexible)
Ensemble Simulation Model Forecasting
  A component of a continuous conceptual model (NWSRFS)
  Continuous real time inputs (temperature, precipitation, forecasts)
  Accounts for soil moisture states (SAC-SMA) - drives runoff efficiency
  Builds and melts snowpack (Snow-17) – output feeds SAC-SMA
  Flexible run date, forecast period, forecast parameters.
  Evolving toward ESP as primary forecast tool at NOAA/RFCs
  Current Calibration period: 1976-2005
Notes: 8
The NWS started making water supply forecasts in the 1940s for the Colorado basin. Eventually these forecasts were expanded to cover most western snow melt dominated basins through cooperation with the NRCS. Seasonal streamflow forecasts tradionally derive nearly all of their skill from current snowpack conditions in the basin. In fact, the NRCS SNOTEL network was deployed beginning in the late 1970s explicitly to improve seasonal streamflow prediction.
Bullets on left give background information on water supply forecasts.
The upper right figure is hyperlinked to “live” website (www.cbrfc.noaa.gov/westernwater). - Suggest clicking on website and giving a brief synopsis of current forecasts for western US. Note that most areas are extremely dry this year – particularly most all of California and the Colorado Basin. The Washington Cascades and the upper Arkansas River Basin are the only areas with above normal forecasts this year.

## Slide 9: ESP Technique
Flow
Time
Future
Now
Past
Low chance of this level flow or higher
High chance of this level flow or higher
Medium chance of this level flow or higher
©The COMET Program
Notes: In another example, past observations are use to adjust the hydrologic model. The current time is when model states are saved. The future will use forecast or historic data as input to the model to produce possible hydrographs. Here, a series of hydrograph traces are generated, each based on a particular set of input values. The resulting traces give an idea of the range of possible flows.
For this case, because all of the traces are above this point, the probability that this flow will occur is very high. For the this second case, there is a medium chance flows at this level will occur since some of the traces were above and below this point. For the third case, chances of this flow are low, since all of the trances are lower than this particular value.

## Slide 10: ESP for Water Supply
ESP forecasts based on
  (1) initial conditions (e.g. snow pack, base flow, etc)
  (2) future scenarios
Early in the season, future scenarios contribute more to forecast
As snow accumulates, dry/wet years begin to define themselves in the initial conditions

## Slide 11: Feb 1 forecast
Snow
Time
Future
Feb 1
Past
Low chance of this level snow or higher
High chance of this level snow or higher
Medium chance of this level snow or higher
©The COMET Program
Notes: In another example, past observations are use to adjust the hydrologic model. The current time is when model states are saved. The future will use forecast or historic data as input to the model to produce possible hydrographs. Here, a series of hydrograph traces are generated, each based on a particular set of input values. The resulting traces give an idea of the range of possible flows.
For this case, because all of the traces are above this point, the probability that this flow will occur is very high. For the this second case, there is a medium chance flows at this level will occur since some of the traces were above and below this point. For the third case, chances of this flow are low, since all of the trances are lower than this particular value.

## Slide 12: Mar 1 forecast
Snow
Time
Future
Mar 1
Past
Low chance of this level flow or higher
High chance of this level flow or higher
Medium chance of this level flow or higher
©The COMET Program
Notes: In another example, past observations are use to adjust the hydrologic model. The current time is when model states are saved. The future will use forecast or historic data as input to the model to produce possible hydrographs. Here, a series of hydrograph traces are generated, each based on a particular set of input values. The resulting traces give an idea of the range of possible flows.
For this case, because all of the traces are above this point, the probability that this flow will occur is very high. For the this second case, there is a medium chance flows at this level will occur since some of the traces were above and below this point. For the third case, chances of this flow are low, since all of the trances are lower than this particular value.

## Slide 13: Apr 1 forecast
Snow
Time
Future
Apr 1
Past
Low chance of this level snow or higher
High chance of this level snow or higher
Medium chance of this level snow or higher
©The COMET Program
Notes: In another example, past observations are use to adjust the hydrologic model. The current time is when model states are saved. The future will use forecast or historic data as input to the model to produce possible hydrographs. Here, a series of hydrograph traces are generated, each based on a particular set of input values. The resulting traces give an idea of the range of possible flows.
For this case, because all of the traces are above this point, the probability that this flow will occur is very high. For the this second case, there is a medium chance flows at this level will occur since some of the traces were above and below this point. For the third case, chances of this flow are low, since all of the trances are lower than this particular value.

## Slide 14: 30 year average
30 year averages are updated once every 10 years
Currently using
  1971-2000 for averages
  1971-2000 for statistical prediction
  1976-2005 for ESP
Update for WY2012 will be based on 1981-2010 averages
Trends in monthly precipitation are important for ESP

## Slide 15
Preliminary Data
18% reduction in mean

## Slide 16: Upper Green (at Warren Bridge) Precipitation Trends by Month
Chart: March precipitation
| 1951.0 | 1952.0 | 1953.0 | 1954.0 | 1955.0 | 1956.0 | 1957.0 | 1958.0 | 1959.0 | 1960.0 | 1961.0 | 1962.0 | 1963.0 | 1964.0 | 1965.0 | 1966.0 | 1967.0 | 1968.0 | 1969.0 | 1970.0 | 1971.0 | 1972.0 | 1973.0 | 1974.0 | 1975.0 | 1976.0 | 1977.0 | 1978.0 | 1979.0 | 1980.0 | 1981.0 | 1982.0 | 1983.0 | 1984.0 | 1985.0 | 1986.0 | 1987.0 | 1988.0 | 1989.0 | 1990.0 | 1991.0 | 1992.0 | 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0
March | 3.929 | 4.118 | 2.184 | 1.479 | 3.908 | 2.017 | 2.245 | 2.131 | 3.357 | 3.576 | 1.977 | 4.294 | 2.334 | 1.813 | 1.049 | 1.215 | 2.802 | 2.119 | 2.341 | 0.689 | 1.861 | 2.808 | 3.03 | 1.112 | 4.591 | 5.385 | 0.251 | 3.971 | 2.389 | 1.898 | 1.608 | 2.533 | 2.001 | 1.218 | 1.671 | 9.55 | 1.981 | 1.751 | 2.082 | 1.34 | 0.991 | 0.991 | 2.415 | 3.98 | 1.896 | 2.575 | 1.897 | 1.463 | 5.031 | 3.835 | 2.329 | 1.257 | 2.082 | 2.022 | 1.568
Chart: February precipitation
| 1951.0 | 1952.0 | 1953.0 | 1954.0 | 1955.0 | 1956.0 | 1957.0 | 1958.0 | 1959.0 | 1960.0 | 1961.0 | 1962.0 | 1963.0 | 1964.0 | 1965.0 | 1966.0 | 1967.0 | 1968.0 | 1969.0 | 1970.0 | 1971.0 | 1972.0 | 1973.0 | 1974.0 | 1975.0 | 1976.0 | 1977.0 | 1978.0 | 1979.0 | 1980.0 | 1981.0 | 1982.0 | 1983.0 | 1984.0 | 1985.0 | 1986.0 | 1987.0 | 1988.0 | 1989.0 | 1990.0 | 1991.0 | 1992.0 | 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0
February | 3.256 | 2.266 | 3.535 | 2.765 | 0.728 | 3.744 | 1.38 | 1.503 | 1.554 | 1.238 | 0.079 | 3.551 | 3.23 | 3.001 | 2.192 | 1.357 | 2.506 | 1.488 | 3.611 | 3.442 | 3.827 | 4.179 | 2.256 | 1.864 | 1.805 | 1.569 | 4.636 | 6.268 | 5.449 | 7.124 | 1.547 | 4.535 | 1.753 | 0.907 | 1.093 | 3.277 | 2.889 | 2.557 | 3.773 | 4.825 | 1.586 | 0.555 | 2.702 | 2.206 | 3.032 | 4.912 | 3.317 | 5.673 | 3.793 | 4.764 | 0.495 | 2.225 | 2.659 | 2.042 | 2.165
Chart: January precipitation
| 1952.0 | 1953.0 | 1954.0 | 1955.0 | 1956.0 | 1957.0 | 1958.0 | 1959.0 | 1960.0 | 1961.0 | 1962.0 | 1963.0 | 1964.0 | 1965.0 | 1966.0 | 1967.0 | 1968.0 | 1969.0 | 1970.0 | 1971.0 | 1972.0 | 1973.0 | 1974.0 | 1975.0 | 1976.0 | 1977.0 | 1978.0 | 1979.0 | 1980.0 | 1981.0 | 1982.0 | 1983.0 | 1984.0 | 1985.0 | 1986.0 | 1987.0 | 1988.0 | 1989.0 | 1990.0 | 1991.0 | 1992.0 | 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0
January | 3.75 | 1.309 | 0.932 | 0.674 | 4.025 | 1.325 | 1.206 | 1.436 | 0.566 | 0.651 | 2.137 | 0.337 | 1.613 | 5.092 | 1.769 | 1.589 | 1.782 | 2.141 | 1.391 | 2.246 | 3.199 | 2.981 | 2.282 | 0.88 | 2.004 | 0.23 | 3.582 | 3.655 | 0.884 | 2.152 | 4.434 | 3.121 | 4.433 | 2.371 | 1.564 | 0.495 | 3.544 | 1.382 | 1.216 | 2.122 | 1.052 | 3.318 | 1.28 | 1.445 | 3.342 | 11.653 | 1.338 | 3.361 | 2.125 | 3.096 | 2.702 | 2.003 | 3.093 | 2.952

## Slide 17: Upper Green (at Warren Bridge) Precipitation Trends by Month
Chart: May precipitation
| 1951.0 | 1952.0 | 1953.0 | 1954.0 | 1955.0 | 1956.0 | 1957.0 | 1958.0 | 1959.0 | 1960.0 | 1961.0 | 1962.0 | 1963.0 | 1964.0 | 1965.0 | 1966.0 | 1967.0 | 1968.0 | 1969.0 | 1970.0 | 1971.0 | 1972.0 | 1973.0 | 1974.0 | 1975.0 | 1976.0 | 1977.0 | 1978.0 | 1979.0 | 1980.0 | 1981.0 | 1982.0 | 1983.0 | 1984.0 | 1985.0 | 1986.0 | 1987.0 | 1988.0 | 1989.0 | 1990.0 | 1991.0 | 1992.0 | 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0
May | 3.443 | 2.963 | 2.68 | 1.996 | 1.33 | 3.463 | 4.607 | 2.926 | 3.193 | 2.97 | 1.404 | 2.923 | 6.718 | 2.405 | 3.238 | 3.048 | 3.216 | 3.213 | 0.534 | 4.508 | 7.288 | 5.751 | 2.741 | 2.313 | 4.196 | 4.034 | 1.315 | 3.052 | 1.302 | 2.062 | 2.308 | 3.539 | 3.129 | 3.504 | 1.38 | 3.376 | 1.234 | 2.533 | 2.184 | 4.142 | 2.553 | 1.649 | 2.881 | 2.369 | 4.317 | 2.737 | 3.091 | 2.266 | 4.714 | 1.624 | 2.142 | 3.355 | 1.298 | 2.674 | 2.492
Chart: April precipitation
| 1951.0 | 1952.0 | 1953.0 | 1954.0 | 1955.0 | 1956.0 | 1957.0 | 1958.0 | 1959.0 | 1960.0 | 1961.0 | 1962.0 | 1963.0 | 1964.0 | 1965.0 | 1966.0 | 1967.0 | 1968.0 | 1969.0 | 1970.0 | 1971.0 | 1972.0 | 1973.0 | 1974.0 | 1975.0 | 1976.0 | 1977.0 | 1978.0 | 1979.0 | 1980.0 | 1981.0 | 1982.0 | 1983.0 | 1984.0 | 1985.0 | 1986.0 | 1987.0 | 1988.0 | 1989.0 | 1990.0 | 1991.0 | 1992.0 | 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0
April | 4.502 | 2.855 | 2.83 | 5.662 | 2.484 | 3.178 | 2.048 | 1.932 | 1.584 | 2.607 | 1.653 | 2.748 | 2.048 | 2.283 | 2.515 | 2.622 | 2.421 | 2.408 | 0.963 | 1.969 | 3.799 | 1.984 | 4.379 | 4.305 | 4.399 | 4.146 | 2.889 | 1.631 | 1.339 | 4.029 | 2.657 | 3.113 | 3.812 | 1.855 | 2.474 | 1.255 | 1.69 | 3.088 | 5.09 | 2.307 | 3.646 | 0.987 | 3.258 | 1.977 | 3.851 | 2.825 | 2.821 | 4.228 | 2.281 | 2.351 | 1.669 | 3.049 | 4.063 | 1.154 | 2.909

## Slide 18: Yampa / White Rivers (updated through 2010)
Chart: Yampa at Steamboat Springs May precipitation
| 1976.0 | 1977.0 | 1978.0 | 1979.0 | 1980.0 | 1981.0 | 1982.0 | 1983.0 | 1984.0 | 1985.0 | 1986.0 | 1987.0 | 1988.0 | 1989.0 | 1990.0 | 1991.0 | 1992.0 | 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0
May | 3.419 | 2.538 | 4.658 | 1.945 | 2.925 | 3.343 | 3.125 | 4.894 | 5.699 | 5.623 | 4.586 | 2.109 | 2.907 | 2.269 | 2.295 | 4.806 | 3.182 | 7.163 | 4.749 | 6.359 | 4.413 | 5.862 | 3.955 | 5.304 | 3.6 | 3.463 | 2.169 | 6.574 | 3.342 | 4.356 | 2.996 | 2.613 | 4.449 | 4.461 | 6.326
Chart: Yampa at Steamboat Springs April Precipitation
| 1976.0 | 1977.0 | 1978.0 | 1979.0 | 1980.0 | 1981.0 | 1982.0 | 1983.0 | 1984.0 | 1985.0 | 1986.0 | 1987.0 | 1988.0 | 1989.0 | 1990.0 | 1991.0 | 1992.0 | 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0
April | 4.124 | 3.022 | 5.03 | 5.355 | 5.334 | 4.682 | 5.934 | 5.722 | 4.701 | 4.283 | 3.458 | 3.43 | 4.539 | 3.709 | 3.298 | 6.272 | 3.133 | 4.452 | 1.792 | 3.66 | 5.303 | 3.231 | 3.825 | 2.403 | 4.698 | 3.73 | 2.792 | 4.23 | 3.553 | 4.185 | 4.358 | 2.607 | 3.338 | 3.808 | 3.859

## Slide 19
Preliminary Data
4% reduction in mean

## Slide 20
Preliminary Data
6% reduction in mean

## Slide 21
Preliminary Data
6% reduction in mean

## Slide 22
Preliminary Data
11% reduction in mean

## Slide 23
Preliminary Data
All 30 year means since 1911-1940

## Slide 24
1981-2010 is the driest 30 year period on record

## Slide 25: Affect on Forecasts
WY2011 forecasts continue to use 1971-2000 means:
  Statistical models (SWS and NRCS) will use 1971-2000
  Simulation model (ESP) will use 1976-2005
WY2012 forecasts will be based on 1981-2010 inputs in both forecast models
  ESP and SWS will both use the same period
SNOTEL network much stronger for 1981-2010 period than in 1970s. This network is critical for forecast skill.
All things equal, these forecasts will be lower since input data sets are drier in the 30 year average
  Especially true in early season forecasts
  Later season forecasts more controlled by observed snowpack
Percent of normal forecast values should remain largely unchanged (since normals AND forecasts will be lower)

## Slide 26: CBRFC Updates
Anticipating significant spring flooding May-June
Migration to new CHPS (Community Hydrologic Prediction Services) software complete late summer / early fall
Experimental hydrologic ensemble services running – incorporates ensemble weather and climate forecasts
Seasonal / 2 year prediction workshop (March 2011) and testbed activity – possible fall workshop to include stakeholders
Evapotranspiration work ongoing – testing application to drought and water demand forecast / analysis

## Slide 27: Discussion
CBRFC will shortly develop plan for implementation of new normal period (bulk of work to occur over summer)
USBR requested update occur on August 1 or on January 1 but not in between
Comments / Questions?

## Slide 28
Kevin Werner
CBRFC Service Coordination Hydrologist
Phone: 801.524.5130
Email: kevin.werner@noaa.gov
www.cbrfc.noaa.gov