## Slide 1: Colorado River District Annual Water Seminar Sept 15, 2011 Grand Junction, CO
Kevin Werner
NWS Colorado Basin River Forecast Center
2011: A Really Big Year

## Slide 2: Outline
River Forecast Center overview
2011 runoff review
Forecast verification
30 year average update

## Slide 3: Colorado Basin River Forecast Center
The Colorado Basin River Forecast Center (CBRFC) generates streamflow forecasts across the Colorado and Utah. The latest forecasts, data, and more are available online:
  Daily streamflow forecasts
  Long lead peak flow forecasts
  Water supply forecasts
  Webinar briefings
  Email updates
  And More….
www.cbrfc.noaa.gov

## Slide 4: Late 2010

## Slide 5: Early 2011
Irrational Exuberance?
Pre Holiday Storm:
Lake Mead up ~2 feet from local runoff
Large snow accumulation
Forecasts reflected that….

## Slide 6
Web Reference: www.cbrfc.noaa.gov/gmap/gmapm.php?wcon=checked
4090/129%
1040/85%

## Slide 7: Spring 2011
  Winter and Spring 2011 were much wetter than normal for most of Utah – especially the months of March/April/May
  Spring was very cold across Utah
  Snowpack accumulated to record or near record amounts at most SNOTEL sites
  Snow melt was delayed – and largely tempered by cool May/June weather
  Flood did occur in low elevation basins (May/June) and high elevation basins (late June/July)

## Slide 8: Spring 2011
  Winter and Spring 2011 were much wetter than normal for most of Utah – especially the months of March/April/May
  Spring was very cold across Utah
  Snowpack accumulated to record or near record amounts at most SNOTEL sites
  Snow melt was delayed – and largely tempered by cool May/June weather
  Flood did occur in low elevation basins (May/June) and high elevation basins (late June/July)

## Slide 9: Spring 2011
  Winter and Spring 2011 were much wetter than normal for most of Utah – especially the months of March/April/May
  Spring was very cold across Utah
  Snowpack accumulated to record or near record amounts at most SNOTEL sites
  Snow melt was delayed – and largely tempered by cool May/June weather
  Flood did occur in low elevation basins (May/June) and high elevation basins (late June/July)

## Slide 10: Spring 2011
  Winter and Spring 2011 were much wetter than normal for most of Utah – especially the months of March/April/May
  Spring was very cold across Utah
  Snowpack accumulated to record or near record amounts at most SNOTEL sites
  Snow melt was delayed – and largely tempered by cool May/June weather
  Flood did occur in low elevation basins (May/June) and high elevation basins (late June/July)
2011 Inflow = 12.9 MAF
163% of normal

## Slide 11: Flooding and High Flows

## Slide 12: Flooding and High Flows
Wettest area was northern Colorado
Upper Colorado also quite wet
Gunnison divided web from normal
Dolores, San Juan basins nearer normal

## Slide 13: Peak Flow Forecasts
Long Lead Peak Flow Forecasts
Snowmelt maximum mean daily flow (April-July)
Probabilistic Forecasts
  Exceedence Probabilities -10%,25%,50%, 75%, 90%
Issued (at least) monthly from March-June (this year weekly starting April 19)
~60 forecast points – some unregulated, some regulated
Daily Forecasts
Full Hydrograph out 14 days
  Includes temperature (10 days) and precipitation (5 days) forecast
  Includes any knowledge of future regulation (e.g. reservoir release)
Single value forecast
Issued daily by 10am MDT and updated throughout day
~450 forecast points

## Slide 14: Yampa: Daily Forecasts
Yampa / White Rivers generally peaked in June
Very high (many records) snowpack
Cool June somewhat mitigated high flows although rivers flowed high for several weeks

## Slide 15: Yampa: Long Lead Peak Forecasts

## Slide 16: Upper Colorado
Upper Colorado includes many high elevation basins that peaked late into June or early July
Near record snowpack caused high flows
High flows were mitigated by cool June temperatures

## Slide 17: Upper Colorado: Long Lead Peak Forecasts

## Slide 18: Gunnison
Gunnison basin divided wet conditions to the north and near average to the south. Hwy 50 was a rough dividing line
Peaks mostly in early June with continued high flows through June and even July (monsoon moisture)

## Slide 19: Gunnison: Long Lead Forecasts

## Slide 20: 2010 Summary
  2011: cool and wet spring made for unique hydrology. Both long lead and daily forecasts performed relatively well.
  More forecast verification:
    Temperature forecasts
    Water supply forecasts
  Forecast Issues
    Struggled with some reservoir release plans in some cases
    Temperature forecasts in late May / early June were much too high causing streamflow forecasts to be too high
  Upcoming CBRFC activities
    November 4 stakeholder forum – Denver, CO
    Annual recap and outlook webinar – Oct/Nov
    Individual meetings with water managers

## Slide 21: 30 year average update
30 year averages are updated once every 10 years
Currently using
  1971-2000 for averages
  1971-2000 for statistical prediction
  1976-2005 for ESP
Update for WY2012 will be based on 1981-2010 averages
Trends in monthly precipitation are important for ESP

## Slide 22
Preliminary Data
18% reduction in mean

## Slide 23
Preliminary Data
4% reduction in mean

## Slide 24
Preliminary Data
6% reduction in mean

## Slide 25
Preliminary Data
6% reduction in mean

## Slide 26
Preliminary Data
11% reduction in mean

## Slide 27
Preliminary Data
All 30 year means since 1911-1940

## Slide 28
1981-2010 is the driest 30 year period on record

## Slide 29: Affect on Forecasts
WY2011 forecasts continue to use 1971-2000 means:
  Statistical models (SWS and NRCS) will use 1971-2000
  Simulation model (ESP) will use 1976-2005
WY2012 forecasts will be based on 1981-2010 inputs in both forecast models
  ESP and SWS will both use the same period
SNOTEL network much stronger for 1981-2010 period than in 1970s. This network is critical for forecast skill.
All things equal, these forecasts will be lower since input data sets are drier in the 30 year average
  Especially true in early season forecasts
  Later season forecasts more controlled by observed snowpack
Percent of normal forecast values should remain largely unchanged (since normals AND forecasts will be lower)

## Slide 30
Kevin Werner
CBRFC Service Coordination Hydrologist
Phone: 801.524.5130
Email: kevin.werner@noaa.gov
Feedback, Questions, Concerns always welcome….