## Slide 1: June 23, 2011
Kevin Werner
NWS Colorado Basin River Forecast Center
NOAA / CBRFC
Water forecasts and data in support of western water management

## Slide 2: Outline
River Forecast Center overview
Water Year 2011

## Slide 3: The Global Water Imperative
Protect Life and Property
Support Economic Security
Water has always been a critical component in the success of any economic endeavor
Protect Health and Environment
Water is the lifeblood of this planet
Triple Threat: Scarcity and floods, climate change, and aging infrastructure
Mitigate Escalating Risk
Floods and droughts cause more U.S. economic losses than any other type of natural disaster
“Nearly half of the streams and lakes in the U.S. are not clean enough to sustain swimming and fishing and our infrastructure has been given a D grade”

## Slide 4: Who we are…
Mission: To understand and predict changes in the Earth’s environment … to meet our Nation’s economic, social, and environmental needs
Mission: The NWS provides weather, hydrologic, and climate forecasts and warnings … for the protection of life and property and the enhancement of the national economy
The Colorado Basin River Forecast Center generates streamflow forecasts and related datasets for the Colorado and eastern Great Basins

## Slide 5: Colorado Basin River Forecast Center
One of 13 River Forecast Centers
Established in the 1940s for water supply forecasting
Three primary missions:
1. Seasonal Water supply forecasts for water management
2. Daily forecasts for flood, recreation, water management
3. Flash flood warning support
www.cbrfc.noaa.gov

## Slide 6: Flood Forecasts / Routine Forecasts
Nominally provided at ~400 points every 6 hours out to 14 days.
Flexible web interface to forecasts and data
Requires large amounts of data (e.g. snow, precip, temps, streamflow)

## Slide 7: Water Supply Forecasts
Generated seasonally
Typically January through June
Updated monthly or as needed
Forecast runoff volume (usually April – July)
Probabilistic

## Slide 8: Water Supply Decision Support
The
past
The
future
Efforts in parallel --
CBRFC working to improve probabilistic flow forecasts
BOR working to implement probabilistic water management model

## Slide 9: General RFC Model
Forecast
precip / temp
Weather and Climate Forecasts
River
Forecast
System
parameters
Observed
Data
Analysis &
Quality Control
Calibration
model
guidance
Hydrologic Model Analysis
hydrologic
expertise &
judgment
Outputs
Graphics
River Forecasts

## Slide 10: RFC Models
Snow Model: SNOW-17 Temperature Index Snow model
RFC forecast uses a snow model and a rainfall-runoff model:
  Snow model: Temperature index model for simulating snowpack accumulation and melt
  Hydrologic model: Conceptual hydrologic model used to generate runoff

## Slide 12
Climate patterns
Rain Gage Measurement
GOES Satellite Estimate
Gridded Precipitation Estimate
Radar Estimate
Forecaster Analysis
Quantitative Precipitation Estimates (QPE)

## Slide 13
Source: water.weather.gov
Source: www.cbrfc.noaa.gov

## Slide 14: Weather and Climate Forecasts
RFC forecast system incorporates both weather and climate forecasts:
  Weather forecasts integrated into daily operations with forecaster control over point and basin average values
    Water supply forecasts typically only use QPF during late season or in lower basin
    When QPF is used, it is used in a deterministic manner
  Climate forecasts integrated into seasonal water supply forecasts through probability shifts of forcing ensemble
    Climate forecasts are typically only considered in lower basin and only in ENSO years

## Slide 15
Observed
Simulated
Forecast hydrograph
‘Adjusted’/‘Forecast’ is a single time series broken into observed and future pieces.
  It equals obs when available, otherwise patterned with sim
  Can control how quickly it blends into the actual values of the sim

## Slide 16
Web Reference: http://www.cbrfc.noaa.gov

## Slide 17: June 1-15 Precipitation
Web Reference: http://water.weather.gov/precip

## Slide 18: Temperature

## Slide 20
June 2 June 9 June 22

## Slide 22: Snow: Bear River Basin
Web Reference: http://www.cbrfc.noaa.gov/station/sweplot/sweplot.cgi???open

## Slide 23: Weather Forecast
Heat is coming!!
Above normal temperatures today, tomorrow, Friday
Slight cooling for Utah over the weekend
Colorado stays warm
<- Today (Thursday)
Saturday PM
Tuesday PM

## Slide 25: Current Forecasts
May 24 Forecasts
June 22 daily Forecasts

## Slide 29: Experimental Daily Ensembles
Ensemble forecasts that incorporate weather forecasts are run daily for Upper Colorado Basin forecast points
Prototype web tool available
Does NOT work correctly downstream of reservoirs yet
NOT available for the Great Basin yet
URL: www.cbrfc.noaa.gov/devel/hefs

## Slide 30
Kevin Werner
CBRFC Service Coordination Hydrologist
Phone: 801.524.5130
Email: kevin.werner@noaa.gov
Feedback, Questions, Concerns always welcome….