## Slide 1
Colorado Basin River Forecast Center
2017 Water Supply Verification / Year in Review
November 14th 2017
Greg Smith
Sr. Hydrologist
Please mute your phone until ready to ask a question - Thank You

## Slide 2
2017 Water Supply Review / Verification Webinar
Why Do Verification?
It’s a path to improvement
Reviewing the season helps us know where to focus efforts
Primary sources of error in the forecast:
Future weather (largest uncertainty and impact)
Hydrology model uses climatology going forward
Extreme future weather results in largest forecast errors
Data Issues (impact model states such as snowpack)
Bad data quality, non-functioning gages, network outages
Data availability, network density
Model calibration limitations
Quality / availability of historical data
Unknown / Ungaged Diversions
Changes in the river basin

## Slide 3
Understanding the forecasts – what are we providing?
Weather recap – primary impacts to the 2017 runoff
Forecasts and verification for key sites – basin highlights
Summary / Conclusion & the next steps toward improvement
2017 Water Supply Review / Verification Webinar

## Slide 4
1981
1982
1983
….
2010
Current hydrologic model states :
River / Res. Levels
Soil Moisture
Snowpack
-> Future Time
Past <-
Start with current conditions of streamflow, soil moisture, snowpack
Apply precipitation and temperature from each historical year used in model calibration (1981-2015) from current date into the future.
A forecast is generated for each of the years (1981-2015) as if, going forward, that year will happen
This creates 35 possible future streamflow patterns. Each year is given a 1/35 chance of occurring
Probabilistic Forecasts

## Slide 5
The flows are summed into volumes for the period of interest(typically April 1 – July 31)
The statistics are simplified
50% exceedance value approximates the most probable forecast. A range of probable outcomes is also provided.
1
2
Ensemble Prediction System (ESP) - Probabilistic Forecasts
3
March 1st 2017 Forecast Guidance for Lake Powell

## Slide 6
The range of probable outcomes are summarized graphically.
These “forecast evolution plots” are updated daily throughout the season
Period: 2017-04-01 – 2017-07-31
10% 15858.69
20% 14425.24
30% 13258.32
40% 12779.66
50% 12272.80
60% 11826.55
70% 11344.69
80% 10844.99
90% 9731.74

## Slide 7
Precipitation: Fall was dry but winter was wet
December – Big Change
Very Dry October
Dry in much of the Upper Colorado & Great Basins. A mix in the Lower Colorado Basin

## Slide 8
Narrow corridor of significant moisture transport in the atmosphere
Mid December through January: significant moisture impacted the western U.S.
In fact winter was Very Wet !

## Slide 9
December-January: Very Wet
February: Continued wet in Green, Great, part of Lower Colorado Basins
December 2016
January 2017
February 2017

## Slide 10
Dec-Feb Precipitation Ranking

## Slide 11
Snow Conditions
SNOTEL ranking for March 6th 2017
Black – Highest on record (upper Gunnison, Dolores, Duchesne, Great Basin, Green above Fontenelle)
Period of record 34-39 years most sites

## Slide 12
Snow Conditions
CBRFC Model Snow for March 6th 2017
Significant Snowpack: Green River Basin, Great Basin, Gunnison River Basin.
Above average snow many other areas.
Significant lower elevation snow in Green River Basin, Gunnison River Basin, Great Basin

## Slide 13
Some daily temperatures 10-25 degrees above average in February and March
Temperature Impacts: Warm later winter / spring temperatures

## Slide 14
Hickerson Park SNOTEL
Elevation: 9,145 Feet
Upper Green River Basin
March Weather – Temperature Impacts
Above average temperatures
Above Freezing
Temperatures
Significant snowmelt
Instantaneous Temperature Plot

## Slide 15
Vail Mountain SNOTEL
Elevation: 10,300 Feet
Colorado River Headwaters
Above average temperatures
Above Freezing
Temperatures
Cooler
temperatures
Instantaneous Temperature Plot
March Weather – Temperature Impacts
Significant snowmelt

## Slide 16
March-May: Generally wetter in northern areas and drier to the south
March 2017
April 2017
May 2017

## Slide 17
March Weather – Impacts to the snowpack

## Slide 18: Low Elevation Snowmelt in March/April
Significant low elevation snowpack melted with above normal temperatures in March. Resulted in record streamflows for the month of March and saturated soil conditions.
Modeled March 1st Snow
March Max Temp Monthly Deviation
Modeled April 1st Snow
Lower elevation areas were saturated prior to runoff due to the melt of a significant low elevation snowpack and rain.

## Slide 19
March Weather Impacts: Record March Runoff
Upper Green
375%
Yampa
135%
Duchesne
190%
Colorado
130%
Lake Powell
167%
Gunnison
120%
Dolores
140%
San Juan
190%
Notable March Volumes
Fontenelle (1/52)* 180 / 343% 99 (1986)
Flaming Gorge (1/55)* 400 / 392% 237 (1997)
Granby (1/90)* 9.7 / 206% 9.1 (2015)
Willow Creek (1/98)* 3.1 / 254% 2.3 (1920)
Green Mtn (1/80)* 14.9 / 153% 14.4 (2015)
Colo-Kremmling (1/55)* 52 / 167% 52 (2015)
Blue Mesa (1/49)* 70 / 193% 55 (1951)
Mcphee(2/37) 57 / 270% 59 (1997)
Vallecito (1/76)* 24 / 285% 16 (2007)
Navajo (4/47) 177 / 191% 198 (1995)
Lemon Res(1/54)* 4.1 / 259% 3.8 (1989)
Lake Powell(3/54) 1109 / 167% 1141 (1985)
Site (Rank/POR) – Mar Vol KAF / % Avg – old record (year)
Many more sites in top 2 or 3 of record
River Basin % average streamflow for March
(approximate)
Data is provisional – not all basin stream flow sites included

## Slide 20
Data is provisional
March % of Average Unregulated Streamflow for March
200%
407%
Notable March Volumes
329%
306%
336%
380%
330%
245%
225%
155%
123%
Bear-UT/WY (1/75)* 5.8 /200% 4.8 (2015)
Smiths Fork (1/75)* 8.8 /224% 6.2 (2015)
Stewart Dam (1/89)* 98 /407% 82 (1986)
Logan River (1/52)* 25 /306% 23 (1986)
Blacksmith Fork (1/99)* 23 /336% 22 (1986)
Little Bear River(1/73)* 29 /380% 24 (1986)
South Fork Ogden (1/94)* 29/400% 25 (1986)
Pineview Inflow (1/79)* 80/330% 72 (1986)
Provo-Woodland(1/52)* 11.6/265% 11.4 (1986)
Provo-Hailstone(1/62)* 18.3/319% 16.5 (1986)
Site (Rank/POR) – Mar Vol KAF / % Avg – old record (year)
Saturated conditions, warm temperatures, low elevation snowmelt and precipitation resulted in record flows at many locations.
Many more sites in top 2 or 3 of record
March Weather Impacts: Record March Runoff
Notes: Lower elevations of the Bear River Basin in northern Utah and southern Idaho are saturated according to the model.
This area has already experienced some flooding issues and will continue to experience very efficient runoff through the sprin

## Slide 21
April Weather Impacts: Record April Runoff
Upper Green
265%
Yampa
105%
Duchesne
200%
Colorado
120%
Lake Powell
152%
Gunnison
155%
Dolores
125%
San Juan
145%
Notable April Volumes
Fontenelle (1/52)* 225 / 264% 180 (1986)
Flaming Gorge (1/55)* 350 / 262% 299 (1969)
Granby (2/90) 26 / 191% 30 (1962)
Willow Creek (2/98) 15 / 357% 16 (1962)
Blue Mesa (1/49)* 145/ 188% 137 (1985)
McPhee(7/37) 95 / 134% 162 (1985)
Vallecito (1/76)* 45 / 192% 42 (2005)
Navajo (8/47) 234 / 138% 392 (1985)
Lemon Res(5/54) 10 / 173% 13 (2005)
Lake Powell(5/54) 1607 / 152% 2708 (1985)
Site (Rank/POR) – Apr Vol KAF / % Avg – old record (year)
At least 9 sites in Upper Green River and Duchesne basins with records
Many more sites in top 5 of record across the area
River Basin % average streamflow for April
(approximate)
Data is provisional – not all basin stream flow sites included

## Slide 22
Extreme wet conditions Dec-Feb
Anticipate large forecast errors with early season forecasts.
Forecasts too low since precipitation received was much above normal.
Dry and very warm conditions developed by March
Forecasts would trend down in many areas – drier than climatology
Forecast errors may be on the high side some areas.
Impacts of the early snow melt in many areas.
Did we shift some of the April-July runoff into March ?
Did the model handle the melt properly – could impact the accuracy of late
season snow states in the model ?
Forecast Verification:
What impacts might we expect from the weather scenario that played out?

## Slide 23
Reds – This years forecast higher than ESP historical model error.
Blues – This years forecast lower than the ESP historical model error.
Blacks – This years forecast similar to the ESP historical model error.
January 2017 Verification Map
April 2017 Verification Map
2017 Forecast Verification Map:
improvement
improvement
worse

## Slide 24
Forecast Verification Plots: So what are we looking for ?
Like to see the observed volume fall within the forecast range (the blue line)
If it does not, it may be due to extreme weather in the future. It may not be a bad forecast. However, It could indicate an error in the model states (snow etc.) or other issues.

## Slide 25
Grey Bars – If we just forecast average every month, this would be the historical error.
Red Bars - The historical forecast error. So we do provide information that is better than just going with average.
2017 error in yellow
Worse than the historical forecast error *
Better than the historical forecast error
Mean Absolute Error
2017 Error Plots: So what are we looking for ?
* does not necessarily mean a bad forecast

## Slide 26: 2017 Forecast/Runoff Impacts
Upper Green River Basin
Early season forecast errors due to extreme wet weather that followed.
Seasonal forecasts and the model performed very well despite concerns of higher forecast uncertainty due to record conditions
Yampa River Basin
Largest forecast errors were in February and March. Errors were primarily weather related as March was very dry and warm.
Seasonal forecasts and the model performed well with no major adjustments required.
Duchesne River Basin
Largest forecast errors were early and again in May. Extreme wet followed by very dry and warm conditions April-June.
Seasonal forecasts and the model guidance too high. Possible model snow states were a little off but conditions were also very dry later in spring.

## Slide 27: Forecast Evolution Plot: Fontenelle Reservoir Inflow
Flaming Gorge
April-July Observed Volumes
APRIL-JULY OBSERVED
1719 KAF/237%
Highest on Record
PREVIOUS RECORD=1683 KAF
Near record snow + saturated soil conditions +June rain event = record runoff!
Mar-Jun weather near normal
Record precipitation Dec-Feb
Notes: Focus on uncertainty
-January forecast. Still a chance for below average volumes
-forecast continued to increase- we can’t forecast extremes the model isn’t going ot handle 3 months of record precipitation well

## Slide 28: Forecast Evolution Plot: Flaming Gorge Inflow
Flaming Gorge
April-July Observed Volumes
APRIL-JULY OBSERVED
2214 KAF/226%
2nd Highest on Record
RECORD=2224 KAF (1986)
April-July volume impacted more by March warm up and snowmelt.
2017 March-July Observed = 2614 KAF
March-July Record (1986) = 2385 KAF
Record precipitation Dec-Feb
Mar-Jun weather near normal
Notes: Focus on uncertainty
-January forecast. Still a chance for below average volumes
-forecast continued to increase- we can’t forecast extremes the model isn’t going ot handle 3 months of record precipitation well

## Slide 29: Forecast Evolution Plot: Yampa River-Maybell
Flaming Gorge
*231%
152%
*Record volume forecasted
APRIL-JULY OBSERVED
799 KAF/85%
1030 KAF
110%
750 KAF
80%
Wet Dec and Jan
Warm dry March and snowmelt
Average Apr-May weather

## Slide 30: Forecast Evolution Plot: Duchesne River-Tabiona
*231%
APRIL-JULY OBSERVED
167 KAF/155%
Record precipitation Dec-Feb
Below average precip
Forecasts were too high from March on.
Conditions were dry but model snow states may have been off.
Storm prior to/during water supply then dried out…..

## Slide 31: Forecast Verification: Fontenelle and Flaming Gorge Inflows
Flaming Gorge
Fontenelle Reservoir Inflow
Flaming Gorge Reservoir Inflow
Notes: Focus on uncertainty
-January forecast. Still a chance for below average volumes
-forecast continued to increase- we can’t forecast extremes the model isn’t going ot handle 3 months of record precipitation well

## Slide 32
Flaming Gorge
*231%
152%
*Record volume forecasted
Forecast Verification:
Yampa - Maybell
Duchesne - Tabiona

## Slide 33: 2017 Forecast / Runoff Impacts
Colorado River Headwaters
Early season forecast errors were better than usual. Forecast errors increased above historical errors most likely due to snow state issues as well as the dry warm March.
Farther downstream (Colorado-Cameo) forecast errors were minimized as upstream errors (too high, too low) cancelled each other out.
Model performed as expected. Issues with the snow states have been identified as due to data limitations. The use of newer SNOTEL sites, once they have a sufficient record, may result in better snowpack representation.

## Slide 34
Williams Fork was the highest forecast (as a percent of average) in the area.
Snow States / Data availability issue
Forecast Evolution Plot: Williams Fork Reservoir
APRIL-JULY OBSERVED
90 KAF/94%
Warm, Dry, Snowmelt
May storm, too much precipitation indicated
Best forecast

## Slide 35
Model performed rather well. Observed volumes fell within the 10/90 forecast range throughout the season.
Forecast Evolution Plot: Eagle Bellow Gypsum
APRIL-JULY OBSERVED
308 KAF/92%
Warm, Dry, Snowmelt

## Slide 36
Model tends to have a low bias. This may be a candidate for recalibration.
Forecast Evolution Plot: Ruedi Reservoir Inflow
APRIL-JULY OBSERVED
140 KAF/101%

## Slide 37: 2017 Forecast/Runoff Impacts
Gunnison
Largest errors were at the beginning of the season. Errors climbed above historical errors late in the season.
Early season errors were explained by the extreme wet weather that followed. Late season errors were due to inaccurate model snow states at the highest elevations. Too much snow melted out of these areas in the model during the very warm periods earlier in spring.
Dolores
Largest errors were February – April, above historical error. These improved later in the season.
Forecast error was easily attributed to a record / near record snowpack that developed early to be followed by very dry and warm conditions March-April.
San Juan
Early season errors due to wet weather that followed. Some late season errors due to snow states at high elevations too low. Animas and eastern tributaries of the San Juan River.

## Slide 38: Forecast Evolution Plot: Blue Mesa Inflow
APRIL-JULY OBSERVED
915 KAF / 136%
Late season snow adjustment
Record precipitation Dec-Feb
Warm, Dry, Snowmelt
Increase in error (compared to historical) late in season. Not enough snow at high elevations of the model

## Slide 39: Forecast Evolution Plot: McPhee Reservoir Inflow
APRIL-JULY OBSERVED
346 KAF / 117%
Warm, Dry,
Snowmelt
Model performed well. No significant adjustments to model states were necessary. Another dry warm spring had significant impacts on evolving forecasts and runoff.

## Slide 40: Forecast Evolution Plot: Vallecito Reservoir Inflow
Very wet Dec-Feb
Forecast declined due to dry March-April. May was wetter. Model performed very well with consistent forecasts mid March forward
APRIL-JULY OBSERVED
214 KAF / 110%

## Slide 41: Forecast Evolution Plot: Navajo Reservoir Inflow
Model state adjustment to add snow
Early season error due to wet weather that followed. Late season error was due to a model snow states being too low in eastern headwaters of the San Juan. (Rio Blanco,Navajo).
APRIL-JULY OBSERVED
778 KAF / 106%

## Slide 42
9600
134%
10400
145%
9300
130%
8800
123%
8300
116%
6500
91%
Forecast Evolution Plot: Lake Powell
Reflected the basin as a whole with early season errors due to wet weather that followed. Forecasts decreased due to warm dry March-April. Overall model performed as expected. Largest error was in March.
APRIL-JULY OBSERVED
8174 KAF / 114%

## Slide 43: 2017 Forecast/Runoff Impacts
Eastern Great Basin
Errors greater than historical existed throughout the forecast season for many sites. Largest errors were early in the season and again in March
Several things contributed to forecast errors larger than the historical errors. Early season errors can be attributed to the extreme wet conditions that followed. Significant snow at lower elevations melted in February and early March due to warm temperatures. Saturated soils and flooding was the result. Models most likely struggled with soil moisture states as well as how much high elevation snow remained later in the season.
Sevier
Errors a little above the historical error Feb-May, however historical errors are generally small in the spring. The dry spring weather may have resulted in a little too much melt out of high elevation snow in the model
Virgin
Forecast errors were below the historical error throughout the season.

## Slide 44
Forecast Evolution Plot: Pineview Reservoir Inflow
Record wet Dec-Feb
APRIL-JULY OBSERVED
178 KAF / 158%
Warm, Dry, Snowmelt
Forecast error was above historical throughout the season. The extreme back and forth weather had a large impact. Model snow states may have been too high.

## Slide 45
Forecast Evolution Plot: Weber River at Oakley
Model performed much better at this higher elevation site.
APRIL-JULY OBSERVED
163KAF / 138%

## Slide 46
Historical errors are low here. Model performed fairly well but may have melted too much high elevation snow during the warm March-April period.
Forecast Evolution Plot: Sevier River at Hatch
APRIL-JULY OBSERVED
58 KAF / 121%
Not enough
snow in model

## Slide 47
Forecast Evolution Plot: Virgin at Virgin
APRIL-JULY OBSERVED
85 KAF / 112%
A good forecast throughout as the forecast / model error was lower than the historical error.

## Slide 48: 2017 Forecast / Runoff Impacts
Lower Colorado – Little Colorado, Gila, Salt, Verde
Forecasts are developed based on current snowpack, soil moisture conditions, ENSO (El Nino outlook), and short term rainfall outlook. Snowpack plays a role but the winter rain events are what really generates the seasonal volumes.
Above average observed Dec-Feb. Weak La Nina conditions gave way to weak El Nino conditions By February. Forecasts correctly called for above median volumes as the season progressed.
Notice the forecast range is quite large, anticipating the potential of winter rain events. A wet period from mid January into February had the largest impact on the forecasts.

## Slide 49
Jan-May OBSERVED
158 KAF / 282% median
Jan-May OBSERVED
458 KAF / 156% median
Forecast Evolution Plots: Lower Colorado River Basin

## Slide 50
Wrapping things up….
2017 observed
April-July runoff volumes
Percent of Average

## Slide 51: Upper Green Snow (Modeled May –July) – Late Melt !
May 1
June 1
July 1
CBRFC MODEL SNOW (% median )
Significant Runoff Areas
March/April warm up did not impact high and mid elevation snow. Significant snow remained through July. Diurnal snowmelt pattern was seen well into summer.
Notes: Melt pattern. Snotels melted out by 6/1

## Slide 52
Issues with precipitation gage. Estimated during winter. May have resulted in model/snow state issues?
Very deep snow in places this year impacted SNOTEL precipitation gages.
Hard to say how significant but impacts to model snow states were possible.
Potential data issues due to deep snow

## Slide 53
SITES WITH 30+ YEARS
ALL SITES
11,300 FT
10,400 FT
8,940 FT
9,400 FT
11,100 FT
JNPC2 installed 2000
MFKC2 installed 2002
FCVC2 installed 2012
11,150 FT
New SNOTEL sites will provide an opportunity to improve model calibrations
Williams Fork Reservoir Basin

## Slide 54
2017 had a little bit of everything – we learn a lot in years like this
We felt we could account for the majority of errors that occurred in the 2017 forecasts
  Extreme weather in the future
    Not much can be done pending more advanced / accurate meteorological guidance
    Adding additional years when recalibrating – wider range of forecast possibilities
    Communicating the situation, uncertainties, and possibilities continue to be important
  Late season high elevation snow not represented well by the model in some areas
    Verify model is handling early season snow melt correctly.
    Attempting to take advantage of newer SNOTEL sites as soon as realistic to do so.
    Working to best use potential satellite snow products (ongoing projects with JPL)
In many ways the model performed very well
  Upper Green River Basin of Wyoming
2018 improvements
  Expand Great Basin calibration period to 35 years (1981-2015)
  Add additional stream forecast segments to the model in the Gunnison Basin
Feedback is always welcome - We are happy to discuss any specific forecast with you.
A first look at 2018 is scheduled for Thursday December 7th at 11 am MT. Please go to cbrfc.noaa.gov and follow the webinars link to register.
2017 Forecast Review / Verification Summary