## Slide 1
CRFS Technical Meeting LC Operations Update
March 27, 2014

## Slide 2
Topics
LC Operations Update
Minute 319 Update

## Slide 3
Lower Basin Operations Water Year 2014
Lake Mead Conditions
Current elevation: 1,103.0 feet (46% full)
Projected 2014 EOCY elevation: 1,086.0 feet
  Projected decline of 22.8 feet in CY 2014
Operating under the Normal/ICS Surplus Condition
  Lower Basin projected water use of 7.5 maf +/- ICS created or delivered
  Mexico projected to take delivery of 1.5 maf +/- any water deferred or delivered
    Environmental pulse flow taking place in Spring 2014 (105 kaf)
      Restoration of the Lower Colorado reach in Mexico

## Slide 4
Lower Basin Side Inflows – WY/CY 20141,2 Intervening Flow from Glen Canyon to Hoover Dam
Month in WY/CY 2014 |  | 5-Year Average Intervening Flow (KAF) | Observed Intervening Flow (KAF) | Observed Intervening Flow (% of Average) | Difference From 5-Year Average (KAF)
HISTORICAL | October 2013 | 52 | 38 | 73% | -14
 | November 2013 | 52 | 116 | 221% | 64
 | December 2013 | 95 | 41 | 43% | -54
 | January 2014 | 75 | 45 | 60% | -30
 | February 2014 | 78 | 76 | 97% | -2
FUTURE | March 2014 | 68 |  |  | 
 | April 2014 | 80 |  |  | 
 | May 2014 | 60 |  |  | 
 | June 2014 | 23 |  |  | 
 | July 2014 | 64 |  |  | 
 | August 2014 | 116 |  |  | 
 | September 2014 | 97 |  |  | 
 | October 2014 | 52 |  |  | 
 | November 2014 | 52 |  |  | 
 | December 2014 | 95 |  |  | 
WY 2014 Totals |  | 860 | 824 | 96% | -36
CY 2014 Totals |  | 860 | 828 | 96% | -32
1 Values were computed with the LC’s gain-loss model for the most recent 24-month study.
2 Percents of average are based on the 5-year mean from 2009-2013.

## Slide 5
Lower Basin Side Inflows – WY/CY 20131,2 Intervening Flow from Glen Canyon to Hoover Dam
1 Values were computed with the LC’s gain-loss model for the October 2013 24-month study.
2 Percents of average are based on the 5-year mean from 2008-2012.

## Slide 6
Lower Basin Side Inflows – WY/CY 20141,2 Intervening Flow from Glen Canyon to Hoover Dam
1 Values were computed with the LC’s gain-loss model for the most recent 24-month study.
2 Percents of average are based on the 5-year mean from 2009-2013.

## Slide 7
Lower Basin Side Inflows 5-year average comparison: 2013/2014

## Slide 8
Lower Basin Side Inflows 5-year average comparison: 2013/2014

## Slide 9
Lower Basin Side Inflows Forecast value comparison: CBRFC vs. USBR

## Slide 10
1,219.6
26.120 maf
Lake Powell
Lake Mead
3,700
24.322 maf
Not to Scale
16.2 maf
9.5 maf
9.6 maf
17.0 maf
1,145
1,075
3,648
3,575
2.5 maf
1.9 maf
Dead Storage
Dead Storage
0.0 maf
0.0 maf
895
3,370
1,105
12.2 maf
5.9 maf
3,525
1,025
6.0 maf
1,082.8 feet
10.2 maf in storage
40% of capacity
3,615.4 feet
13.3 maf in storage
55% of capacity
End of Water Year 2014 Projections March 2014 24-Month Study Most Probable Inflow Scenario1
7.48 maf
Projected Unregulated Inflow into Powell = 11.80 maf (109% of average)
1 WY 2014 unregulated inflow into Lake Powell is based on the CBRFC outlook dated 3/4/14.

## Slide 11
1,219.6
26.120 maf
Lake Powell
Lake Mead
3,700
24.322 maf
16.2 maf
9.5 maf
9.6 maf
17.0 maf
1,145
1,075
3,648
3,575
2.5 maf
1.9 maf
Dead Storage
Dead Storage
0.0 maf
0.0 maf
895
3,370
1,105
12.2 maf
5.9 maf
3,525
1,025
6.0 maf
End of Calendar Year 2014 Projections
March 2014 24-Month Study Most Probable Inflow Scenario1
1,085.99 feet
10.5 maf in storage
40% of capacity
3,611.4 feet
12.9 maf in storage
53% of capacity
1 WY 2014 unregulated inflow into Lake Powell is based on the CBRFC outlook dated 3/4/14.
Not to Scale

## Slide 13
Percent of Traces with Event or System Condition Results from January 2014 CRSS1,2 (values in percent)
 | Event or System Condition | 20143 | 2015 | 2016 | 2017 | 2018
Upper Basin – Lake Powell | Equalization Tier | 0 | 17 | 23 | 31 | 29
 | Equalization – annual release > 8.23 maf | 0 | 17 | 22 | 31 | 29
 | Equalization – annual release = 8.23 maf | 0 | <1 | 1 | <1 | <1
 | Upper Elevation Balancing Tier | 0 | 50 | 51 | 45 | 42
 | Upper Elevation Balancing – annual release > 8.23 maf | 0 | 8 | 30 | 34 | 31
 | Upper Elevation Balancing – annual release = 8.23 maf | 0 | 42 | 21 | 11 | 11
 | Upper Elevation Balancing – annual release < 8.23 maf | 0 | <1 | <1 | <1 | <1
 | Mid-Elevation Release Tier | 100 | 33 | 17 | 13 | 18
 | Mid-Elevation Release – annual release = 8.23 maf | 0 | <1 | <1 | 1 | 1
 | Mid-Elevation Release – annual release = 7.48 maf | 100 | 33 | 17 | 12 | 17
 | Lower Elevation Balancing Tier | 0 | <1 | 9 | 11 | 11
Lower Basin – Lake Mead | Shortage Condition – any amount (Mead ≤ 1,075 ft) | 0 | <1 | 44 | 54 | 53
 | Shortage – 1st level (Mead ≤ 1,075 and ≥ 1,050) | 0 | <1 | 43 | 44 | 31
 | Shortage – 2nd level (Mead < 1,050 and ≥ 1,025) | 0 | <1 | 1 | 9 | 18
 | Shortage – 3rd level (Mead < 1,025) | 0 | <1 | <1 | 1 | 4
 | Surplus Condition – any amount (Mead ≥ 1,145 ft) | 0 | <1 | 4 | 7 | 13
 | Surplus – Flood Control | 0 | <1 | <1 | 1 | 2
 | Normal or ICS Surplus Condition | 100 | >99 | 52 | 39 | 34
1 Reservoir initial conditions based on observed levels on December 31, 2013
2 Hydrologic inflow traces based on resampling of the observed natural flow
record from 1906-2010
3 Percentages shown in 2014 are reported as ‘0’ as 2014 operations were
determined by the August 2013 24-Month Study

## Slide 14
Additional Operational Data (provisional year-to-date values)
Mexico Excess Flows
  3,886 acre-feet (as of 3/26/14)
Brock Reservoir Total Storage
  35,800 acre-feet (as of 3/22/14)
Senator Wash Total Storage
  13,800 acre-feet (as of 3/22/14)

## Slide 15: Minute 319: Pulse Flow

## Slide 16
Lower Colorado River
Operations
For further information: http://www.usbr.gov/lc/region
Email at:
bcoowaterops@usbr.gov