## Slide 1
USBR Updates:
Green River
CRFS Meeting March 27, 2014

## Slide 2: Green River Operations
Fontenelle
Flaming Gorge

## Slide 3: Fontenelle Operations

## Slide 4: Fontenelle
Storage
Live Capacity 345,000 AF
Capacity on 3/26/14 127,317 AF
(37% full) slightly high for March
Pool Elevation
Reservoir Elev. (Min) 6506.00 feet
Elevation on 3/26/14 6472.07 feet
Elevation above (Min) 33.93 feet
Inflow and Release
Average Inflow 925 cfs
Average Release 1,430 cfs

## Slide 5: Fontenelle Reservoir Elevation
Notes: Go to P:\FontenelleOps\FontenelleDailyOps.xls to get most recent plot

## Slide 6: Fontenelle Inflow and Release
Apr – Jul Inflow
1,240 KAF (171%)
Projected releases between 3,000-8,000 cfs over summer, likely longer duration of 8,000 cfs, depends on observed inflow
Notes: Go to P:\FontenelleOps\FontenelleDailyOps.xls to get most recent plot

## Slide 7: Flaming Gorge Operations

## Slide 8: Flaming Gorge
Live Capacity 3.752 MAF
Capacity on 3/26/14 2.909 MAF
Available Space .843 MAF
(78% full)
Reservoir Elev. 6040.00 feet
Elevation on 3/26/14 6017.99 feet
Elevation below (Full) 22.01 feet
Average Inflow 1,750 cfs
Average Release 830 cfs

## Slide 9
Spring 2014 Hydrograph
Apr – Jul Inflow
1,430 KAF (146%)
Projected releases steady of approximately 2,000 cfs over summer and winter
Projected peak between 4,600-8,600 cfs for 3-4 weeks during larval drift

## Slide 10: Upper Green Classifications

## Slide 11: Yampa River Classifications

## Slide 13: Green WY 2014
Fontenelle releases expected to be higher this summer and the reservoir is expected to fill.
Flaming Gorge peak release timed with larval trigger. Runoff conditions may require releases prior to larval presence. Maximum summer releases vary between 3,000 cfs, 4,600 cfs and 8,600 cfs. Current base flow releases calculated at 1,975 cfs.