## Slide 1: CBRFC UPDATE
CRFS
December 8, 2015

## Slide 2: Overview
HEFS
Web page changes
  Monthly precipitation maps
  New front page map overlays
    Seasonal Weather
    Soil Moisture
  Upper Colorado Situational Awareness page
ESP baseflow verification

## Slide 3: HEFS Hydrologic Ensemble Forecast System
LEGACY ESP
Precipitation
  0 or 5 days QPF
  climatology from calibration
Temperature (max/min)
  10 days max/min QTF
  climatology from calibration
Post-processing
  Schaake – monthly timestep
  Lower Basin – trace weighting based on ENSO condition
HEFS ESP
Precipitation
  15 days from GEFS ensemble mean
  270 days from CFS ensemble mean
  climatology
Temperature (max/min)
  15 days from GEFS ensemble mean
  270 days from CFS ensemble mean
  climatology
Pre-processor
  converts single trace mean forecasts from GEFS and CFS back into ensembles based on historical relationship between hindcasts and calibration data
Post-processing
  EnsPost – daily time step

## Slide 4: HEFS Initial Verification Results Upper Basin
Animas - Durango
East - Almont
Elk - Milner
Green – Warren Bridge

## Slide 5: GEFS/CFSv2 Precipitation Skill Lower Basin
Salt – Roosevelt
CFSv2
GEFS
Gila – Gila
Verde – Horseshoe
Virgin – Virgin

## Slide 6: HEFS Initial Verification Conclusions
Little, if any, skill added with GEFS/CFS forecast in Upper Basin
  not unexpected given not much skill in CFSv2 precip forecasts
  need to do more analysis on a monthly scale
Does adding GEFS/CFS improve forecasts in Lower Basin?
  have begun running real time this year
  will run reforecasts and analyze results in the next few months
How does CFS forecast fare when looking at ENSO signal?
  limited sample size so it will be difficult to draw any conclusions
Full presentations from October 2015 Stakeholder meeting:
  http://www.cbrfc.noaa.gov/present/2015/forum/GEFSCFS.pdf
  http://www.cbrfc.noaa.gov/present/2015/forum/postadjust.pdf

## Slide 7: WEB PAGE Monthly/Seasonal Precipitation Maps
Lumped areas based on CBRFC model defined sub-areas vs. HUC
Can be ‘trimmed’ to display most important areas for runoff contribution
  more representative of how water supply conditions have been affected
  these trimmed areas can then be used to compute the monthly %average precipitation
Added additional increments to %average scale for better resolution of extreme events
Available as an overlay on front page map

## Slide 8
LEGACY
NEW

## Slide 9
 | OCT | NOV | DEC | JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | WYR TOT
HUC | 44 | 96 | 122 | 64 | 82 | 61 | 85 | 254 | 143 | 155 | 92 | 61 | 102
TRIMMED BASIN | 51 | 113 | 113 | 44 | 75 | 55 | 70 | 218 | 100 | 139 | 83 | 58 | 91
NRCS | 48 | 114 | 111 | 46 | 74 | 58 | 65 | 227 | 101 | 138 | 81 | 64 | 90
Water Year 2015
Monthly %AVG
Precipitation above
Lake Powell

## Slide 10: WEB PAGE New Front Map Overlays
Seasonal Precipitation (Water Year)
Monthly Precipitation
Month To Date
Full and trimmed versions
Fall Model Soil Moisture
Current Model Soil Moisture
Current Model ‘Inches to Saturation’
Full and trimmed versions

## Slide 11: WEB PAGE Model Soil Moisture

## Slide 12: WEB PAGE