## Slide 1: Evaluating Utah Energy Balance Snowmelt Model in Operational Forecasting
John A Koudelka
David Tarboton
Utah State University
3/26/2015

## Slide 2: Bio
MS in Remote Sensing & GIS - University of Wisconsin, 2006
Research Scientist at the Idaho National Laboratory - GIS applications and Spatial Databases
PhD student with Dr David Tarboton at Utah State University

## Slide 3: Overview
Purpose
Utah Energy Balance (UEB) Snowmelt Model
Preliminary Study
Next Steps

## Slide 4: Motivation
Gage | Historic Peak1 | Average Peak1 | Flood Flow1 | Forecasted Exceedence Probability1 |  |  |  |  | Normal Time of Peak1 | Issue Date1 | 2010 Mean Daily2 | 2010 Mean Date2 | 2010 Peak Flow3 | 2010 Peak Date3
 |  |  |  | 90% | 75% | 50% | 25% | 10% |  |  |  |  |  | 
Weber (OAWU1) | 4170 | 1625 | 2790 | 1250 | 1350 | 1500 | 1650 | 1750 | 5/24 - 6/16 | 5/19 | 2600 | 6/7 | 3530 | 6/10
Bear (BERU1) | 2980 | 1610 | 4390 | 1050 | 1150 | 1300 | 1500 | 1700 | 5/22 - 6/14 | 5/19 | 2390 | 6/8 | 3240 | 6/8
Blacks Fork (LTAW4) | 6970 | 2440 | 5500 | 860 | 1020 | 1150 | 1450 | 2100 | 5/2 - 6/27 | 5/19 | 4070 | 6/14 | 4280 | 6/14
Elk Nr Milner (ENMC2) | 6290 | 4160 | 4200 | 2750 | 3000 | 3450 | 3850 | 4200 | 5/19 - 6/12 | 5/19 | 6100 | 6/8 | 6970 | 6/8
1. CBRFC mean daily forecasts for June, 2010. http://www.cbrfc.noaa.gov/wsup/pub2/peak/peak.php?year=2010&month=c
2. Mean Daily Peaks. http://waterdata.usgs.gov/
3. Yearly peaks. http://www.cbrfc.noaa.gov/gmap/info/info.php?type=peaks&idcol=id&station=OAWU1
*all values in cfs
CBRFC models were not able to duplicate streamflow peaks in the 2010 Spring runoff.
Believed to be due to incorrect simulation of snowpack

## Slide 5: 2010 Daily Mean Streamflow Observations

## Slide 6: 2010 Snotel Observations

## Slide 7: Questions
Can operational streamflow forecasts be improved by using a distributed, physically-based snowmelt model instead of a temperature index model?
  Is a UEB capable of improving CBRFC streamflow predictions using NWS forecast data?
    SNOW17 uses temperature melt factors
    UEB uses a physical energy balance driven by radiation, temperature, wind, and humidity
  Can UEB run in the FEWS/CHPS application?

## Slide 8: Approach
Select forecast period (0.5 - 3 months) and define an error metric/forecast skill score
Quantify skill using forecast data and SNOW17
Quantify skill using best retrospective data and SNOW17
Quantify skill using best retrospective and UEB
→ 2 vs 3 indicates uncertainty due to precip forecast uncertainty
→ 3 vs 4 indicates potential improvement due to UEB
Evaluation must be performed in FEWS so that inputs and underlying hydrologic model (SAC) is identical across comparisons.

## Slide 9: Utah Energy Balance Model Overview
Physically based calculation of snow energy balance.
  Predictive capability in changed settings
  Strives to get sensitivities to changes right
Simplicity. Small number of state variables and adjustable parameters.
  Avoid assumptions and parameterizations that make no difference
Transportable. Applicable with little calibration at different locations.
Match diurnal cycle of melt outflow rates
Match overall accumulation and ablation for water balance.
Distributed by application over a spatial grid.
Effects of vegetation on interception, radiation, wind fields

## Slide 10: Utah Energy Balance Snowmelt Model
e.g. Mahat, V. and D. G. Tarboton, (2012), "Canopy radiation transmission for an energy balance snowmelt model," Water Resour. Res., 48: W01534, http://dx.doi.org/10.1029/2011WR010438.
Notes: Physically based calculation of snow energy balance.
  Predictive capability in changed settings
  Strives to get sensitivities to changes right
Simplicity. Small number of state variables and adjustable parameters.
Transportable. Applicable with little calibration at different locations.
Match diurnal cycle of melt outflow rates
Effects of vegetation on interception, radiation, wind fields

## Slide 11: UEB Model Structure
State Equations
  Surface mass and energy balance (beneath the canopy)
Canopy mass and energy balance
State Variables
    Surface snow water equivalent, Ws
    Internal energy of the surface snowpack, Us
    Canopy snow water equivalent, Wc

## Slide 12: UEB Data Requirements
Parameters
  thermal conductivities, emissivity, scattering coefficients, etc.
Initial Conditions
  SWE, Snow Age, energy content, atmospheric pressure, etc.
Spatially Varying, Time Constant (SVTC)
  Slope, Aspect, LAI, CCAN, HCAN, Watershed(s)
Spatially Varying, Time Varying (SVTV)
  Temperature, Precipitation, Wind Speed, Humidity, Radiation

## Slide 13: File-Based Input-output System
Overall control file
Input Files
Watershed file
Provides watershed ID for each grid from the NetCDF file
Site Initial file
Provides site and initial condition values, or points to 2-D NetCDF files where these are spatially variable
Provides start, end and time step, and info. on time varying inputs as either from text file for domain, from 3-D NetCDF file where spatially variable, or constant for all time
Parameter file
Provides parameter Values
Input Control file
2-D NetCDF files
Provides spatially variable site and initial condition values
3-D NetCDF files
Provides input variables for each time step and each grid point
Time series text file
provides input variables for each time step and assumes a constant value for all the grid points
Point detail text file
Aggregated Output Control
Holds list of variables for which aggregated output is required
3-D NetCDF files
Holds a single output variable for all time steps and for entire grid.
Aggregated Output text file
Holds aggregated output
Output Control file
Indicates which variables are to be output and the file names to write outputs.
Holds all output variables for all time steps for a single grid point
Output Files

## Slide 14: UEB Outputs
Precip in the form of rain
Precip in the form of snow
SWE
Surface Sensible Heat Flux
Surface Latent Heat Flux
Surface Sublimation
Average Snow Temperature
Snow Surface Temperature
Energy Content
Total outflow (Rain and Snow)
Canopy interception capacity
Canopy SWE
Canopy Latent and Sensible heat fluxes
Melt from Canopy
etc.

## Slide 15: Preliminary Study
Do we lose important information about the terrain at low resolution?
  NWS gridded data at 800m
How does UEB perform with observed data?
  Run UEB using observed data from TWDEF
How does UEB perform with best available data?
  Run UEB using a mix of Forecast data and best retrospective radiation, rh, and wind data available at TWDEF location
What if radiation data is not available as a forecast product?
  Run UEB using a mix of Forecast data, radiation from Bristow-Campbell calculations, and rest from best available retrospective.

## Slide 16: Study Location

## Slide 17: SVTC Inputs - Resolution
800m
30m
Slope, Aspect, NLCD (LAI, HCAN, CCAN)

## Slide 18: Resolution Comparisons

## Slide 19: Inputs
Observed data (TWDEF)
  Temperature and Precipitation from SNOTEL.
    Precip smoothing
      Avanzi, Francesco, et al. "A processing–modeling routine to use SNOTEL hourly data in snowpack dynamic models." Advances in Water Resources 73 (2014): 16-29.
  Wind, RH, SW, LW from TWDEF sensors
Forecast Data (NLDAS)
  800m Temperature and Precipitation from CBRFC.
  SW, LW, Wind, RH generated from NASA Land Data Assimilation (NLDAS) Forcing2 datasets, regridded to 800m.
Forecast Data with Bristow Campbell (Bristow)
  800m Temperature and Precipitation from CBRFC
  Wind, RH generated from NLDAS
  Model run in BC mode

## Slide 20: Input Comparisons
-10
0
10
20
20
0
-20
Temperature – Monthly Avg
Temperature – Daily Avg
Deg C

## Slide 21: Input Comparisons
0.0
0.1
0.2
0.06
0.03
0.00
1.5
1.0
0.5
0.0
Precipitation – Monthly Sum
Precipitation – Daily Sum
Precipitation Cumulative
meters
meters

## Slide 22: Input Comparisons
0.0
0.6
1.0
1.0
0.6
0.0
Relative Humidity – Monthly Average
Relative Humidity – Daily Average

## Slide 23: Input Comparisons
0
3
6
12
6
0
Wind Speed – Monthly Average
Wind Speed – Daily Average
Meters/second

## Slide 24: Input Comparisons
0
4e+06
6e+06
5000
15000
25000
35000
1e+06
6e+06
2e+06
0
Shortwave – Monthly Sum
Shortwave – Daily Sum
Shortwave – Cumulative
kJ/m2

## Slide 25: Input Comparisons
550000
900000
700000
30000
20000
8e+06
4e+06
0
Longwave – Monthly Sum
Longwave – Daily Sum
Longwave – Cumulative
kJ/m2

## Slide 26: Outputs
0.0
0.8
0.4
meters

## Slide 27: Outputs
-5e+06
0
1e+07
6e+05
-2e+05
0
Energy Content – Monthly Sum
Energy Content – Daily Sum
kJ/m2

## Slide 28: Outputs
0.00
0.03
0.07
0.6
0.3
0.0
Total Outflow – Monthly Sum
Total Outflow – Daily Sum
meters

## Slide 29: Outputs
0.2
0.0
0.1
0.2
0.0
0.1
0.05
0.02
0.00
0.06
0.03
0.00
meters
meters
Precipitation in the form of Rain – Monthly Sum
Precipitation in the form of Rain – Daily Sum
Precipitation in the form of Snow – Daily Sum
Precipitation in the form of Snow – Monthly Sum

## Slide 30: Next Steps
Fully integrate UEB into FEWS/CHPS
Understand GFE products that can be used to run UEB
Evaluate UEB performance for Spring 2010 Runoff event in the Bear and Weber Basins.
  NSE, RMSE, Percent Bias for streamflow outputs compared against SNOW17 and UEB.
Fix problems in UEB to improve performance

## Slide 31: QUESTIONS?
The End
john.koudelka@gmail.com
dtarb@usu.edu